## Slide 1: Unit 16
Programmable Logic Controller （PLC）

## Slide 2
Translation
Reading more
Translating skills
Text
Programmable Logic Controller （PLC）

## Slide 3
Programmable Logic Controller （PLC）
A programmable logic controller, PLC , or programmable controller is a small computer used for automation of real-world processes, such as control of machinery on factory assembly lines. The PLC usually uses a microprocessor. The program can often control complex sequencing and is often written by engineers. The program is stored in battery-backed memory and/or EEPROMs.
PLCs have the basic structure, shown in Fig. 16-1.
可编程逻辑控制器，PLC，或者称可编程控制器，它是一种小型计算机，可用于自动化生产，比如控制工厂的装配机械等。可编程控制器通常使用了微处理器进行控制。其程序可控制复杂的加工工序，并由工程师编写。程序通常存储在随机存储器和（或）电可擦写可编程只读存储器中。
PLC的基本结构如图16-1所示。

## Slide 4
Fig. 16-1 Schematic of a PLC

## Slide 5
From the figure, the PLC has four main units：the Programme memory, the Data memory, the Output devices and the Input devices.
The Programme memory is used for storing the instructions for the logical control sequence. The status of switches, interlocks, past values of data and other working data is stored in the Data memory.
从图中可见，PLC有4个主要的部件：程序存储器，数据存储器，输出设备和输入设备。程序存储器用来存储逻辑控制序列指令。开关状态，联锁状态、历史数据其他工作数据存储在数据存储器中。

## Slide 6
The main differences from other computers are the special input/output arrangements. These connect the PLC to sensors and actuators.
PLCs read limit switches, temperature indicators and the positions of complex positioning systems. Some even use machine vision.
与其他计算机比较，最大的区别是PLC有专用的输入/输出装置。这些装置将PLC与传感器和执行机构相连接。PLC能读取限位开关、温度指示器和复杂定位系统的位置信息。有些甚至使用了机器视觉。

## Slide 7
On the actuator side, PLCs drive any kind of electronic motor, pneumatic or hydraulic cylinders or diaphragms, magnetic relays or solenoids.
The input/output arrangements may be built into a simple PLC, or the PLC may have external I/O modules attached to a proprietary computer network that plugs into the PLC.
执行机构方面，PLC能驱动任何一种电机、气压或液压缸、薄膜装置、电磁继电器或螺线管。输入/输出装置可能是安装在 PLC 内部，或者通过外部I/O模块与专用的计算机网络相连。

## Slide 8
PLCs were invented as less expensive replacements for older automated systems that would use hundreds or thousands of relays and cam timers. Often, a single PLC can be programmed to replace thousands of relays.
Programmable controllers were initially adopted by the automotive manufacturing industry, where software revision replaced the rewiring of hard-wired control panels.
用可编程控制器替代要使用成百上千个继电器和凸轮的早期的自动控制系统更加实惠。一台PLC经常可以通过编程来替代数千个继电器。可编程控制器已在自动化的制造工业中使用，在那里通过对软件的修改可以取代硬连线控制面板的重新连线。

## Slide 9
The functionality of the PLC has evolved over the years to include typical relay control, sophisticated motion control, process control, distributed control systems and complex networking.
可编程控制器经过数年的发展，其功能包括典型的继电器控制，复杂的运动控制，过程控制，分布控制系统和复杂的网络技术。

## Slide 10
The earliest PLCs expressed all decision making logic in simple ladder logic inspired from the electrical connection diagrams. The electricians were quite able to trace out circuit problems with schematic diagrams using ladder logic. This was chosen mainly to reduce the apprehension of the existing technicians.
最早的PLC采用简单的梯形图来描述其逻辑程序，梯形图源自于电气连线图。电气技师们使用逻辑图很容易找出原理图中的电路问题。这样大大减少了技术人员的忧虑。

## Slide 11
Today, the PLC has been proven very reliable, but the programmable computer still has a way to go. With the IEC 6ll31-3 standard, it is now possible to program these devices using structured programming languages, and logic elementary operations.
A graphical programming notation called Sequential Function Charts is available on certain programmable controllers.
如今，PLC的功能已经非常可靠，但是可编程计算
机仍然有其发展空间。依照国际电工委员会的61131-3
标准，现在PLC可以使用结构化的编程语言和逻辑初等
变换来进行编程。
某些可编程控制器可使用一种图表式的编程符号，这种符号称为顺序功能图表。

## Slide 12
However, it should be noted that PLCs no longer have a very high cost (of­ten thousands of dollars) , typical of a “generic” solution. Modern PLCs with full capabilities are available for a few hundred USD.
然而，值得注意的是，PLC不再是非常昂贵的产品（通常是数千美元），而成了一种普通的产品。如今，功能完善的PLC也只要数百美元。

## Slide 13
There are other ways for automating machines, such as a custom microcontroller-based design, but there are differences among both: PLCs contain everything needed to handle high power loads right out of the box, while a microcontroller would need an electronics engineer to design power supplies, power modules, etc.
Also a microcontroller based design would not have the flexibility of in-field programmability of a PLC. That is why PLCs are used in production lines, for example.
使机床实现自动化还有其他的方法，比如传统的基于微控制器的设计，但是这两者之间有一些差别。PLC包含所有能直接操作大功率负载的输出功能。而微控制器还需要专用的电源和电源模块等。同时微控制器设计的方式不具备PLC现场可编程的灵活性。那也正是PLC在生产线上运用的原因之一。

## Slide 14
These typically are highly customized systems so the cost of a PLC is low compared to the cost of contacting a designer for a specific, one-time only design. On the other-hand, in the case of mass-produced goods, customized control systems quickly pay for themselves due to the lower cost of the components.
PLC 控制系统是一些典型的高度用户化的系统，所以与一次请一个设计人员作一个专门的设计比起来，一台PLC的成本要低一些。另一方面，在大批量生产中，因为其构件成本低廉，采用的用户化系统能很快收回成本。

## Slide 15
New words and phrases
actuator ['æktjueitə] n. 执行机构；激励者；促动器
pneumatic [nju:'mætik] adj. 气动的；有气胎的；充气的n. 气胎
hydraulic [hai'drɔ:lik] adj. 水力的；液压的；水力学的
solenoid ['səulənɔid] n. 螺线管；螺线形电导管
proprietary [prəu'praiətəri] n. 所有权；所有人adj. 所有的；专利的
sensor ['sensə] n. 传感器
apprehension ['æpri'henʃən] n. 理解；逮捕；恐惧；忧惧
module ['mɔdju:l] n. 模数；模块；组件
trace out 描绘出
oscillate ['ɔ:sileit] vt. 使动摇；使振荡 vi. 振荡；摆动

## Slide 16
Technical Terms
battery-backed memory 随机存储器
EEPROM 电可擦写可编程只读存储器
Distributed Control Systems 分布式控制系统
IEC 国际电工委员会
ladder logic 梯形图
Sequential Function Charts 顺序功能图
power supply 电源

## Slide 17
Language points
1. A programmable logic controller, PLC, or programmable controller is a small computer used for automation of real-world processes, such as control of machinery on factory assembly lines.
可编程逻辑控制器，PLC ，或者称可编程控制器，它是一种小型计算机，可用于自动化生产，比如控制工厂的装配机械等。
句中used for automation of real-world processes是过去分词短语作后置定语，修饰computer。
例如：1) The boy named John is my friend.
那个叫约翰的男孩是我朋友。

## Slide 18
2) I like reading the novels written by Mark Twain.
我喜欢读马克吐温写的小说。
3) Prices of goods bought through a computer can be lower than store prices.
通过电脑购买的商品视为价格要比商店里商品视为价格低。
以上几个例句的斜体部分都是过去分词短语作后置定语，修饰前面相对应的名词

## Slide 19
2. These connect the PLC to sensors and actuators
这些装置将PLC与传感器和执行机构相连接。
connect：[kə'nekt]
vt.: 1. 连接；联结；接合：
The two cities are connected by a railway. 一条铁路连接起这两个城市。
2. 使联合；使发生联系；使联姻：
A good student must connect what he reads with what he sees around him. 好学生必须会把他在书本里读到的东西与他在周围所看到的事物联系起来。
3. 给…接通电话，用通信工具与…联系(常与with连用)：
The operator will connect you with our sales department. 接线员将把电话给您接到我们的销售部。
你应当先把软管连接在水龙头上然后再打开水源。

## Slide 20
4. 接通(电源)；接通(水源)；接(线)：
You should connect the hose to the tap and then turn on the water. vi : 1. 连接，联结：
The parlour connects with the study. 客厅与书房相连。
2. (火车、公共汽车等)衔接；连续；联运(常与 with 连用)：This early bus from the village connects with the 8:30 train. 从村里发出的这趟早班公共汽车正好与8：30的火车衔接上。
3. 【体育】完全击中球、靶等：
to connect for a home run 击出本垒打
connection [kə'nekʃən] n. 连接；关系；连接件

## Slide 21
3. The input/output arrangements may be built into a simple PLC, or the PLC may have external I/O modules attached to a proprietary computer network that plugs into the
PLC.输入/输出装置可能是安装在 PLC 内部，或者通过外部I/O模块与专用的计算机网络相连。
句中attached to a proprietary computer network是过去分词短语作后置定语来修饰external I/O modules，that plugs into the PLC是定语从句，that在句中作主语，先行词是computer network（专用的计算机网络）。

## Slide 22
external [ik'stə:nəl] adj. 外部的；表面的；[药]外用的；
e.g. 1) There are two big forces at work, external and internal.
工作中有两大影响因素，外部的和内部的。
2) She sets great store by external politeness. 她很注重表面的虚礼。
3) The medicine is for external use, not to drink. 这药是外用的，不可内服。

## Slide 23
4. The earliest PLCs expressed all decision making logic in simple ladder logic inspired from the electrical connection diagrams.
最早的PLC采用简单的梯形图来描述其逻辑程序，梯形图源自于电气连线图。
express [ik'spres]
vt. 表达；快递
to express an idea clearly
清楚地讲述(或表达)一个想法
Her face expressed sorrow.
她的脸上表露出悲哀。
to express a package or merchandise 快运包裹或货物
n. 快车
I’ll take the 11:00 am express to Nanjing .我将乘坐上午11点开往南京的快车。
When does the express to Shanghai leave? 到上海的快车几点离站？

## Slide 24
ladder logic 梯形图
The electricians were quite able to trace out circuit problems with schematic diagrams using ladder logic.
该电工是相当能追查出电路的问题与示意图使用阶梯逻辑。
For instance, the programming of PLCs still relies on a conventional programming style with ladder logic diagrams. 举例来说， PLC的编程仍然依靠传统的编程风格与梯形逻辑图。
The control loop is a continuous cycle of the PLC reading inputs, solving the ladder logic, and then changing the outputs. 控制回路是PLC读取输入的不断循环，解析梯形图逻辑，然后更改输出。

## Slide 25
5 trace [treis]
vi. 追溯；沿路走
The friendly relationship between the two countries traces back to the last century. 两国间的友好关系追溯到上个世纪。
vt. 追踪，查探；描绘；回溯
The murderer was traced to Paris. 那个凶手被追踪到巴黎。
They tried to trace the rumour to its source. 他们试图追查谣言的根源。
They have traced the plan of the construction site. 他们已经画出工地平面图。

## Slide 26
n. 痕迹，踪迹；微量；迹线；缰绳
force into the traces迫使做枯燥无味工作；迫使做日常琐碎的工作
work in the traces循规蹈矩地工作，死板地工作
trace out 画出(或勾画出)…的路线(或轮廓等);草拟：
to trace out the plan of a building 勾画出建筑物的平面图
to trace out a policy 草拟一项政策
The powerhouse was trace out accurately later on a large scale map.
这张房屋图纸是按比例绘制的，只有一个部分不合比例。

## Slide 27
flexible ['fleksibl] adj. 灵活的；柔韧的；易弯曲的
I just want to make it more flexible.
我只是想把它变得更灵活一些。
A good plan must be a little flexible so that special projects can be done well.
一个好的计划一定要灵活一些，这样才能做好一些特殊的项目。
Die with flexible punch was fixed in press with large power buffer to clamp the edge of blanks.
装有活动凸模的模具安装在大功率缓冲器的压力机上以夹紧毛坯的边缘。

## Slide 28
flexibility n.灵活性；弹性；适应性
After each tightening, rotate the crankshaft to check its flexibility.
每拧紧一次，应回转曲轴，以检查灵活性。
The application demonstrates that this component possesses favorable commonality and flexibility.
应用实例表明该组件具有良好的通用性和灵活性。

## Slide 29
I．Answer the following questions according to the text．
How many parts does the PLCs consist of?
2. What functions can PLCs perform?
3. What is the programming language of PLC?
Exercises
The functions of PLCs include typical relay control, sophisticated motion control,
process control, Distributed Control Systems and complex networking.
The PLC has four main units：the Programme memory, the Data memory, the Output devices and the Input devices.
The programming language of PLC is structured programming
languages, and logic elementary operations.

## Slide 30
II．Judge the following are true (T) or false (F) according to the text．
1. The instructions for the logical control sequence are stored in the Data memory.
2. The I/O modules only can be built into PLCs.
3. Now, we can use structured programming languages, and logic elementary operations to program.
4. The simple ladder logic inspired from the electrical connection diagrams.
5. The programmability of a PLC is flexible.
（F）
（F）
（T）
（T）
（T）

## Slide 31
III．Translate the following sentences into English．
1．可编程控制器通常使用了微处理器进行控制。
2．PLC能读取限位开关、温度指示器和复杂定位系统的位
置信息。
3．最早的PLC采用简单的梯形图来描述其逻辑程序。
4．PLC包含所有能直接操作大功率负载的输出功能。
The PLC usually uses a microprocessor.
PLCs read limit switches, temperature indicators and the
positions of complex positioning systems.
The earliest PLCs expressed all decision making logic in simple ladder logic.
PLCs contain everything needed to handle high power loads right out of the box.

## Slide 32
Translating Skills
介词的译法
在英语中，介词(preposition)虽然是一种小词，但在文
中却起到了中介和连接作用。在翻译过程中，介词的翻译
如果处理不好，就无法表达某些最基本的思想或概念。在
科技英语的翻译中，除了一些常用短语已有译法外，大量
介词需要从其基本意义出发，联系上下文加以灵活处理。
下面我们将对常见的几种基本译法加以探讨。

## Slide 33
Ⅰ 转译法
英语中常用介词来表达动作意义。汉译时，将介词转译成动词的情况一般有以下几种：
1. 在作表语的介词短语中
This machine is out of repair． 这台机器失修了。
2. 在作目的或原因状语的介词短语中
The letter E is commonly used for electromotive force.
电动势通常用E这个字母表示。

## Slide 34
3. 在作条件、方式或方法状语的介词短语中
But even the larger molecules with several hundred atoms are too small to
be seen with the best optical microscope． 即使有几百个原子的分子也是太小了，用最好的光学显微镜也看不见它们。
4. 介词短语作补足语时
Heat sets these particles in random motion． 热量使这些粒子作随机运动。

## Slide 35
Ⅱ 增译法
根据介词的含义及上下文语境，同时考虑汉语的惯用表达法，增加译词。
例如：That’s all there is to it．那就是与此有关的全部内容。
The engineer was taken ill with consumption．It was flour on the lungs，the doctor told him at the time． 这个工程师得了肺病、那是由于面粉对肺部的影响．当时医生这样对他说的。（在本句中on=effect)
由此可见，在翻译过程中，熟悉介词与动词或形容词的习惯搭配对于增词并正确理解词义至关重要。

## Slide 36
Ⅲ 省略译法
省略翻译是在确切表达原文内容的前提下使得译文简练且合乎汉语规范．决不是任意删减或省略。以下几种情况，介词可以不译：
1 表示手段、方法的介词
There are four seasons in a year． —年有四季。
2 表示情况的介词
It is known to all that everything in the universe is in constant motion and constant change. 大家都知道宇宙万物都在不断运动变化。
3 介词如for(为了……)，from (从……)，to (对……)，on(在…… 时)等
The barometer is a good instrument for measuring air pressure．
气压计是测量气压的好仪器。

## Slide 37
4 表示与主语有关的某一方面、范围或内容的介词
Something has gone wrong with the engine． 这台发动机出了毛病。
5 在句中作定语的of
The change of electrical energy into mechanical energy is done in motors．
电能变为机械能是通过电动机实现的。(句中of短语和change在逻辑上有主谓关系，可译成主谓结构。)

## Slide 38
Ⅳ 反译法
有的介词短语在翻译过程中必须采用反译法，如不从反面着笔，译文就有可能不通，在这里列举出以下几种情况：
1 在beyond, past，against 等表示超过某限度的能力或反对时
Radio telescopes have been able to probe space beyond the range of ordinary optical telescopes．
射电望远镜已能探测普通光学望远镜达不到的宇宙空间。
2 在of，from等表示地点，距离时
The boat sank of the coast． 这只船在离海岸不远处沉没了。
3 在but，except，besides等表示“除去、除外”时
Copper is the best conductor but silver． 铜是仅次于银的最优导体。

## Slide 39
PLC Programming

## Slide 41
PLC Programming
The first PLCs were programmed with a technique that was based on relay logic wiring schematics. This eliminated the need to teach the electricians, technicians and engineers how to program a computer. But this method has stuck and it is the most common technique for programming PLCs today. An example of ladder logic can be seen in Fig. 16-2. To interpret this diagram we can imagine that the power is on the vertical line on the left hand side, we call this the hot rail. On the right hand side is the neutral rail.
PLC编程
最初PLC编程是采用与继电器逻辑原理图相同的技术(梯形图)，这样电工、技术员和工程师都不需要学习计算机编程。但是这种方法被普遍接受了，成为今天PLC编程的最通用的技术。图16-2给出一个梯形图，为了说明这个图，我们可以想象左边的竖线为电源线，称为火线，右边的是零线。

## Slide 42
In the figure there are two rungs, and on each rung there are
inputs or combinations of inputs (two vertical lines) and outputs
( circles). If the inputs are opened or closed in the right
combination the power can flow from the hot rail, through the
inputs, to power the outputs, and finally to the neutral rail. An
input can come from a sensor, or switch. An output will be some device outside the PLC that is switched on or off, such as lights or motors. In the top rung the contacts are normally open and normally closed, which means if input A is on and input B is off, then power will flow through the output and activate it. Any other combination of input values will result in the output X being off.
图中有两条通路，每一条通路上都有输入或输入的组合(两条水平
线)和输出(圆形符号)，如果通过适当组合便输入是闭合的，电流就
可以从火线通过输入，流过输出最终到零线。输入可以来自传感器
或开关。输出可以是PLC外接的一些器件，它控制如灯或电动机的合
上或断开。在第1条通路中连接一个常开和一个常闭，如果输入A是
合上(则A动作，其常开触点成为闭合)，B是断开(则B不动作，其常
闭触点仍为闭合)，则电流会流过输出并使输出有效。而任何其他输
入的组合(另3种分别为：A合上，B合上；A断开，B合上；A断开，
B断开)都会使(第一条通路不通)输出X是断开的。

## Slide 43
Fig. 16-2 an example of ladder logic diagram

## Slide 44
The second rung of Fig. 16-2 is more complex, there are actually multiple combinations of inputs that will result in the output Y
turning on. On the left most part of the rung, power could flow
through the top if C is off and D is on. Power could also (and
simultaneously) flow through the bottom if both E and F are
true. This would get power half way across the rung, and then if G or H is true the power will be delivered to output Y.
图16-2的第2条通路比较复杂，有多个可能的输入组合会使输
出Y接通。在通路左部，上面一条如果C断开，D接通电流可
以流过，下面一条，如果E和F都接通电流也可以流过，这时
电流流过半条通路，如果还有G或H接通则电流就流到输出端Y了。

## Slide 45
There are other methods for programming PLCs. One of the
earliest techniques involved mnemonic instructions. These
instructions can be derived directly from the ladder logic diagrams and entered into the PLC through a simple programming terminal. An example of mnemonics is shown in Fig. 16-3. In this example the instructions are read one line at a time from top to bottom. The first line 0 has the instruction LDN (input load and not) for input 00001. This will examine the input to the PLC and if it is off it will remember a 1 (or true), if it is on it will remember a 0 (or false).
PLC编程还有其他方法，其中最早的技术之一是符号指令。这
些指令可以直接从梯形图中导出，通过一条简单的编程引脚输
给PLC。图16-3是符号指令的一个例子，在这个例子中，可以
从顶部到底部，每次读一条通路得到符号指令。第0行是对输入
端00001的指令LDN(输入加载并取反)。这条指令会检查输入端
00001，如果是断开就输给PLC一个1(或真)，如果端入端接通就输给PLC一个0(或假)。

## Slide 46
The next line uses an LD (input load) statement to look at the
input 00002. If the input is off it remembers a 0, if the input is on it remembers a 1. The AND statement recalls the last two numbers
remembered and if they are both true the result is a 1, otherwise
the result is a 0. The process is repeated for lines 00003 and
00004, the AND in line 5 combines the results from the last LD instructions. The OR instruction takes the two numbers now remaining and if either one is a 1 the result is a 1, otherwise the result is a 0. The last instruction is the ST (store output) that will look at the last value stored and if it is 1, the output will be turned on, if it is 0 the
output will be turned off.
下一条用LD(输入加载)语句来检测输入端00002，如果输入端是
断开就记为0，如果输入为通电则记为1。AND语句是把上两条
语句的值相“与”，如果都为真则结果为l，否则结果为0。对
00003和00004的输入处理过程相同，第5行AND指令把后两个
LD指令的输出值相“与”得到一个输出值。OR指令对保留的两个
值进行“或”运算，如果任何一个为1，输出为1，否则结果为0。
最后的指令是ST(存储输出)，会把最终的输出值存储起来，如果
是1则输出端为通电，如果是0则输出端为断开。

## Slide 47
Fig. 16-3 mnemonic & equivalent ladder logic program

## Slide 48
The ladder logic program in Fig. 16-3 is equivalent to the
mnemonic program. Even if you have programmed a PLC with ladder logic, it will be converted to mnemonic form before being
used by the PLC.
图16-3的梯形图与代码程序等效，即使
你是用梯形图编程的，也要把它转换成
代码形式输给PLC，PLC才能执行。

## Slide 49
Exercise
I．Answer the following questions according to the text．
What is the first programming language of PLC?
2. How many rail in the ladder logic?
3. What is the input signal of the PLCs?
The first PLCs is ladder logic which was based on relay logic wiring schematics.
There are two rails in the ladder logic.
The input signal of the PLCs is two vertical lines

## Slide 50
4. What is the output signal of the PLCs?
5. what is the different of ladder logic and mnemonic?
The output signal of the PLCs is circles.
Mnemonic can be derived directly from the ladder logic diagrams and entered into the PLC through a simple programming terminal.

## Slide 51
II．Translate the following sentences into Chinese ．
This eliminated the need to teach the electricians, technicians and engineers how to program a computer.
2. An output will be some device outside the PLC that is switched on or off, such as lights or motors.
这样电工、技术员和工程师都不需要学习计算机编程
输出可以是PLC外接的一些器件，它控制如灯或电动机的合上或断开。

## Slide 52
3. One of the earliest techniques involved mnemonic instructions.
4. These instructions can be derived directly from the ladder logic diagrams and entered into the PLC through a simple programming terminal.
其中最早的技术之一是符号指令。
这些指令可以直接从梯形图中导出，通过一条简单的编程引脚输给PLC。

## Slide 53
第十六单元 可编程逻辑控制器
可编程逻辑控制器，PLC，或者称可编程控制器，它是一种小
型计算机，可用于自动化生产，比如控制工厂的装配机械。
可编程控制器通常使用了微处理器进行控制。其程序可控制
复杂的加工工序，并由工程师编写。程序通常存储在随机存
储器和（或）电可擦写可编程只读存储器中。
PLC的基本结构如图16-1所示。

## Slide 54
从图中可见，PLC有4个主要的部件：程序存储器，数据存储器，输出设备和输入设备。程序存储器用来存储逻辑控制序列指令。开关状态，联锁状态、数据的初始值等其他工作数据存储在数据存储器中。

## Slide 55
与其他计算机比较，最大的区别是PLC有专用的输入/输出装置。这些装置将PLC与传感器和执行机构相连接。PLC能读取限位开关、温度指示器和复杂定位系统的位置信息。有些甚至使用了机器视觉。执行机构方面，PLC能驱动任何一种电机、气压或液压缸、薄膜装置、电磁继电器或螺线管。输入/输出装置可能是安装在 PLC 内部，或者通过外部I/O模块与专用的计算机网络相连。用可编程控制器替代要使用成千上百个继电器和凸轮的早期的自动控制系统更加实惠。一台PLC经常可以通过编程来替代数千个继电器。可编程控制器已在自动化的制造工业中使用，在那里通过对软件的修改可以取代硬连线控制面板的重新连线。

## Slide 56
可编程控制器经过数年的发展，其功能包括典型的继电器
控制，复杂的运动控制，过程控制，分布控制系统和复杂的网
络技术。最早的PLC采用简单的梯形图来描述其逻辑程序，梯
形图源自于电气连线图。电气技师们使用逻辑图很容易找出原
理图中的电路问题。这样大大减少了技术人员的忧虑。
如今，PLC的功能已经非常可靠，但是可编程计算机仍然有
其发展空间。依照国际电工委员会的61131-3标准，现在PLC
可以使用结构化的编程语言和逻辑初等变换来进行编程。
某些可编程控制器可使用一种图表式的编程符号，这种符
号称为顺序功能图表。

## Slide 57
然而，值得注意的是，PLC不再是非常昂贵的产品（通常是数千美元），而成了一种普通的产品。如今，功能完善的PLC也只要数百美元。使机床实现自动化还有其他的方法，比如传统的基于微控制器的设计，但是这两者之间有一些差别。PLC包含所有能直接操作大功率负载的输出功能。而微控制器还需要专用的电源和电源模块等。同时微控制器设计的方式不具备PLC现场可编程的灵活性。那也正是PLC在生产线上运用的原因之一。PLC 控制系统是一些典型的高度用户化的系统，所以与一次请一个设计人员作一个专门的设计比起来，一台PLC的成本要低一些。另一方面，在大批量生产中，因为其构件成本低廉，采用的用户化系统能很快收回成本。

## Slide 58
PLC编程
最初PLC编程是采用与继电器逻辑原理图相同的技术(梯形图)，这样电工、技术员和工程师都不需要学习计算机编程。但是这种方法被普遍接受了，成为今天PLC编程的最通用的技术。图16-2给出一个梯形图，为了说明这个图，我们可以想象左边的竖线为电源线，称为火线，右边的是零线。
阅读材料

## Slide 59
图中有两条通路，每一条通路上都有输入或输入的组合(两条水平线)和输出(圆形符号)，如果通过适当组合便输入是闭合的，电流就可以从火线通过输入，流过输出最终到零线。输入可以来自传感器或开关。输出可以是PLC外接的一些器件，它控制如灯或电动机的合上或断开。在第1条通路中连接一个常开和一个常闭，如果输入A是合上(则A动作，其常开触点成为闭合)，B是断开(则B不动作，其常闭触点仍为闭合)，则电流会流过输出并使输出有效。而任何其他输入的组合(另3种分别为：A合上，B合上；A断开，B合上；A断开，B断开)都会使(第一条通路不通)输出X是断开的。

## Slide 60
图16-2的第2条通路比较复杂，有多个可能的输入组合会使输出Y接通。在通路左部，上面一条如果C断开，D接通电流可以流过，下面一条，如果E和F都接通电流也可以流过，这时电流流过半条通路，如果还有G或H接通则电流就流到输出端Y了。

## Slide 61
PLC编程还有其他方法，其中最早的技术之一是符号指令。这些指令可以直接从梯形图中导出，通过一条简单的编程引脚输给PLC。图16-3是符号指令的一个例子，在这个例子中，可以从顶部到底部，每次读一条通路得到符号指令。第0行是对输入端00001的指令LDN(输入加载并取反)。这条指令会检查输入端00001，如果是断开就输给PLC一个1

## Slide 62
PLC编程还有其他方法，其中最早的技术之一是符号指令。这些指令可以直接从梯形图中导出，通过一条简单的编程引脚输给PLC。图16-3是符号指令的一个例子，在这个例子中，可以从顶部到底部，每次读一条通路得到符号指令。第0行是对输入端00001的指令LDN(输入加载并取反)。这条指令会检查输入端00001，如果是断开就输给PLC一个1(或真)，如果端入端接通就输给PLC一个0(或假)。

## Slide 63
下一条用LD(输入加载)语句来检测输入端00002，如果输入端是断开就记为0，如果输入为通电则记为1。AND语句是把上两条语句的值相“与”，如果都为真则结果为l，否则结果为0。对00003和00004的输入处理过程相同，第5行AND指令把后两个LD指令的输出值相“与”得到一个输出值。OR指令对保留的两个值进行“或”运算，如果任何一个为1，输出为1，否则结果为0。最后的指令是ST(存储输出)，会把最终的输出值存储起来，如果是1则输出端为通电，如果是0则输出端为断开。

## Slide 64
图16-3的梯形图与代码程序等效，即使你是用
梯形图编程的，也要把它转换成代码形式输给
PLC，PLC才能执行。

## Slide 65
Thank you!