## Slide 1
Unit 9
Electric Power System Monitoring

## Slide 2
Translation
Reading More
Translating skills
Text
Electric Power System Monitoring
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring

## Slide 3
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
Electric Power System Monitoring

## Slide 4
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
A modern electric power system is an assembly of many components, each of which influences the behavior of every other part.
Proper functioning of the system as a whole makes it necessary to monitor conditions existing at many different points on the system in order to assure optimum operation.
现代供电系统是许多部分的组合，每个部分都影响其他部分的运转。为使系统作为整体正常运作，有必要监控系统中许多不同位置的情况，才能确保最佳运转。

## Slide 5
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
The concern of the customers is primarily that the frequency and voltage of the supply are held within certain rather narrow limits.
Since frequency of the system is the same everywhere, it may be monitored by a single frequency meter located at any convenient point. In contrast, the voltage of the system may be quite different at different points.
Consequently, it is necessary to make continuous observation of the voltage at certain key points in the system in order to provide acceptable service.
用户主要关心的是频率和把供电电压限制在某些相当有限的范围内。因为在任何地方系统的频率都相同，所以可在任一方便的地方安装单个的频率测试仪来监控。相反，系统的电压可能在不同的地方差别很大。因此，必须在系统某些关键位置对电压不断进行观察，才能提供令人满意的服务。

## Slide 6
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
Efficient operation of the system is obtained by assigning proper load schedules to each of the generators of the system.
Newer plants, although individually more efficient, may be located at points of the system where their loading occasions large system losses.
It is desirable to operate with such a division of the load between generators so that the total cost of fuel consumed is minimized.
To provide reliability of the power supply in the event of unexpected conditions, it is desirable for all machines in operation to have the total kilowatt rating somewhat greater than the total load plus losses.
将合适的负荷计划分配给系统中每台发电机，才能使系统达到高效运转。新的设备虽然单机效率较高，但它们在系统中被安装的位置可能会由于它们的加载而造成系统巨大的损失。应该将负荷在发电机之间分配后进行运作，才能使所消耗燃料的费用总额降至最低。为在意外情况下可靠供电，最好使运行中的所有机器的千瓦定额比负荷加上损耗的总数高一些。

## Slide 7
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
Instrumentation is necessary to permit billing of customers for energy used. Many interconnections exist between different power systems.
Instruments must be provided at interchange points to permit billing for energy transferred from one system to another. The continuous monitoring of energy transfer is necessary to assure that interchanged power is within the limits of contract agreements.
The continuous measurement of conditions of major pieces of equipment is necessary to avoid damage due to overload. Instrumentation serves as a guide for future construction in a growing power system.
要想把用户的用电量记入账目，就必须安装测试设备。在不同的供电系统间存在着许多互连。必须在连接点配备测量仪器才能将从一个系统转换到另一个系统的能量记入账目。必须对能量转换不断监测，才能保证交换的电力在协议规定的限度之内。
要避免由于超载造成的损害，必须对大件装置的状态不断测量。测试设备在未来扩充供电系统的建设中起指导作用。

## Slide 8
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
Occasionally, under emergency conditions, a system operator observes that his system load exceeds the ability of the available generating and transmission equipment. He is then faced with the problem of load shedding or, more properly, load conservation.
It is then necessary to drop selected loads where service interruption is least objectionable. In such an event, he relies on the many instruments which provide information relative to system-operation conditions.
有时在紧急情况下，一位系统操作人员注意到他的系统负荷超过了现有发电和输电设备的能力。于是他就面临着限制用电的问题，更恰当地说，是保持负荷的问题。于是就有必要在最合适中断供电服务的地方减少一定的负荷。在此情况下，他依赖于许多测试仪表来提供有关系统运行状况的信息。

## Slide 9
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
Instruments may sound alarms as advance warnings of conditions requiring action to avoid damage to equipment operating beyond its design limitation.
In the event of extreme conditions such as power-system faults, defective equipment is switched out of service automatically.
Instruments that continuously monitor current, voltage, and other quantities must be able to identify the faulted equipment and to bring about operation of the circuit breakers which remove it from service, while leaving in service all other equipment on the operating system.
当要求采取操作避免超过限定运行设计给设备带来损害时，测量仪会发出警报声，作为提前警告。万一出现最糟的情况，如电力系统出现故障，有毛病的设备将会自动关闭，停止运行。要对电流、电压和其他量的测量仪器进行监控，必须能够辨别出产生故障的设备，使断路器开始起作用并将有故障的设备排除在供电服务之外，而让运行系统中其他所有设备继续运行。

## Slide 10
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
The many different electrical devices in a power system and those owned by the customers are designed for operation within certain specified ranges.
Operation outside these designed limits is undesirable, as it may result in inefficiency of operation, excessive deterioration, or (in extreme cases) the destruction of the device.
Careful attention to the conditions under which equipment is operating may indicate corrective action that must be taken.
电力系统和用户拥有的许多不同的电力装置都是为在某些特定范围内运行而设计的，不可以在设计限定范围之外运行，因为它会导致低效运行、过度磨损或者（在极端的情况下）设备损坏。认真观察设备运行状态才会知道应该如何采取正确行动。

## Slide 11
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
Overcurrent is undesirable for all electrical devices, as it produces excessive temperatures, inefficient operation, and reduced service life. Overcurrent in residential circuits may bring about disconnection of the circuit by fuse or breaker action. Overcurrent in motors may also damage insulation.
所有电力装置都不可以过电流，因为这会导致温度过高、低效运行并减少使用寿命。居民电路若电流过载，会导致因熔丝烧断而产生断路，或使断路器动作。电动机若电流过载，会损坏绝缘，使绝缘失效。

## Slide 12
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
New words and phrases
assembly [ə'sembli] n. 装配组件; 装配; 安装
function ['fʌŋkʃən] v. 起作用; 运转
monitor ['mɔnitə] v. 持续观察; 记录或测试（某物）的运作
optimum ['ɔptiməm] adj. 最佳的; 最适宜的; 最有利的
frequency ['fri:kwənsi] n. 振动频率; 波段; 屡次; 频繁
obtain [əb'tein] v. 获得, 得到; 通行, 流行
assign [ə'sain] v. 分配，指派，指定
occasion [ə'keiʒn] v. 致使，惹起，引起
division [di'viʒn] n. 分; 分割; 划分; 歧异, 差别, 分化现象
minimize ['minimaiz] v. 使减(缩)小到最低；极力贬低，最低估计
instrumentation [,instrumen'teiʃən] n. 仪表化，测试设备
interconnection [,intəkə'nekʃən] n. 互相连络
interchange [,intə'tʃeindʒ] v. 交换事物, 互换

## Slide 13
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
kilowatt ['kiləwɔt] n. 千瓦
exceed [ik'si:d] v. 超过，越出
shed [ʃed] v. 去掉; 除掉; 脱落;剥落;蜕下
defective [di'fektiv] adj. 有缺点的; 不完美的; 不完全的
indicate ['indikeit] v. 指示; 指出; 标示; 在仪表盘上显示出
insulation [,insju'leiʃən] n. 绝缘
deterioration [di,tiriə'reiʃən] n. 恶化，降低，退化
result in 结果是；导致
rely on 依靠;信赖
contract agreement合同协议书
bring about 导致,引起
in contrast 于此相反

## Slide 14
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
Technical Terms
frequency meter 频率计
transmission equipment 输电设备
power system fault 电力系统故障
circuit breaker 断路器
service interruption 停电

## Slide 15
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
Notes to the text
1. Proper functioning of the system as a whole makes it necessary to monitor conditions existing at many different points on the system in order to assure optimum operation.
为使系统作为整体正常运作，有必要监控系统中许多不同位置的情况，才能确保最佳运转。
it在句中作形式宾语，句子的真正宾语是to monitor conditions existing at many different points on the system. 当不定式（短语）、动名词（短语）或从句在某个句子中作宾语时，为保持句子结构平衡，避免句式结构的混乱，常用it作形式宾语，而将真正的宾语放在句尾。此时it仍只起先行引导作用，本身无词义。例：
The new method makes it possible to complete the task faster.
新方法使得更快地完成任务成为可能。
We consider it our duty to support good leaders. 我们认为支持优秀领袖是我们的义务。

## Slide 16
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
2. It is desirable to operate with such a division of the load between generators so that the total cost of fuel consumed is minimized.
应该将负荷在发电机之间分配后进行运作，才能使所消耗燃料的费用总额降至最低。
句中，so that引导一个目的状语从句，consumed是过去分词作定语，来修饰限定the total cost of fuel。类似的句子还有：
We must adapt our thinking to the changed conditions.
我们必须使我们的思想适应改变了的情况.
The concert given by their friends was a success.
他们朋友举行的音乐会大为成功.

## Slide 17
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
3. In such an event, he relies on the many instruments which provide information relative to system-operation conditions.
在此情况下，他依赖于许多测试仪表来提供有关系统运行状况的信息。
句中，which引导一个定语从句，在从句中作主语，定语从句的先行词是instruments。

## Slide 18
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
4. Instruments that continuously monitor current, voltage, and other quantities must be able to identify the faulted equipment and to bring about operation of the circuit breakers which remove it from service, while leaving in service all other equipment on the operating system.
要对电流、电压和其他量的测量仪器进行监控，必须能够辨别出产生故障的设备，使断路器开始起作用并将有故障的设备排除在供电服务之外，而让运行系统中其他所有设备继续运行。
句中，that引导一个定语从句，在从句中作主语。equipment后的and连接两个相同句子成分，分别是be able to identify the faulted equipment 和be able to bring about operation of the circuit breakers. which 在句中引导另外一个定语从句，先行词是the circuit breakers，which在从句中作主语。

## Slide 19
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
5. Careful attention to the conditions under which equipment is operating may indicate corrective action that must be taken..
认真观察设备运行状态才会知道应该如何采取正确行动。
句中，这是一个介词＋关系代词来引导的定语从句，句子语序原本应为：the conditions which equipment is operating under。但是由于under和operating不能构成固定的介词短语，因此必须把under提前，放在which前面。

## Slide 20
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
Exercises
I．Answer the following questions according to the text.
1. Why do we have to monitor the electric power system?
2. What’s the function of the instrumentation in the electric power system?
3. How can we monitor the frequency and the voltage of the electric power
system?
4. What will the overcurrent causes for all the electrical devices and the
residential circuits?

## Slide 21
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
II．Judge the following are true (T) or false (F) according to the text.
1. We can monitor the voltage of the power system at any convenient point.（ ）
2. Overcurrent can produce excessive temperatures, inefficient operation, and reduced service life for all electrical devices. ( )
3. To provide reliability of the power supply in the event of unexpected conditions, it is desirable for all machines in operation to have the total load plus losses somewhat greater than the total kilowatt rating. ( )
4. In order to avoid damage due to overload, we have to monitor the conditions of major pieces of equipment occasionally. ( )
5. The many different electrical devices in a power system and those owned by the customers are designed for operation within certain specified ranges. Operation outside these designed limits is undesirable. （ ）
Ex. II.
1.F 2.T 3.F 4.F 5.T

## Slide 22
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
Ⅲ. Translate the following expressions into English.
1. 频率计
2. 输电设备
3. 电力系统故障
4. 断路器
5. 停电
6. 系统负载
7. 限电；减载；甩负荷
8. 电气设备
1. frequency meter
2. transmission equipment
3. power system fault
4. circuit breaker
5. service interruption
6. system load
7. load shedding
8. electrical equipment

## Slide 23
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
IV. Put the following sentences into English.
1. 司机不得超过每小时五十五英里的最大时速
2. 企业必须密切关注社会的变化和需求，以便更好地承担社会责任。
3. 我们要应对这些挑战，最重要的是靠发展。
4. 注意力要集中在获得所需答案应做的工作上。
Ex. IV.
1. Drivers must not exceed a maximum of 55 miles an hour.
2. A business must monitor changes and needs in society in order to behave
in a social responsible way.
3. To meet these challenges, most importantly, we should rely on
development.
4. Attention was focused on what was needed to obtain the required answer.

## Slide 24
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
Translating Skills
科技英语词汇的结构特征（II）
④ 缩略：把词省略或简化，然后组合成新词。现在的趋势是缩略词的数目不断增大，使用面不断扩大。例如：
laboratory截短成lab(实验室)；
Unidentified flying object缩合成UFO(不明飞行物)； ’
Radio detection and ranging缩减成radar(雷达)；
transistor和receiver各取一部分，组合成transceiver(收发机)；
motor＋hotel→motel(汽车旅店)；
mechanics＋electronics→mechatronics(机电学)；
Telecommunications satellite缩略为Telesat(通信卫星)。

## Slide 25
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
(4) 英语科技文体中有很多词汇并不是专业术语，且在日常口语中用得不是很多，它们多见于书面语中，叫做文语词。掌握这类词对阅读科技文献或写科技论文十分重要。这类词用得很广，它们不仅出现在各专业的科技文体中，也出现在政治、经济、法律、语言等社会科学的文体中，例如：
accordance(按照)，imply(隐含)，acknowledge(承认)，inclusion(包括)，alter(改变)，incur(招致)，alternative(交替的)，indicate(指示)，amend(修正)，induce(归纳)，application(应用)，initial(初始的)，appropriate(恰当的)，modification(修改)，attain(达到)，nevertheless(然而)，circumstance(情况)，nonetheless(然而)，compensation(补偿)，obtain(获得)，confirm(证实)，occur(发生)，consequence(后果)，omission(省略)，considering(鉴于)，providing(假设)，consist(组成)，reduce(减少)，constitute(构成)，replacement(代替)，consume(消耗)，specifically(具体地说)，deduce(推理)，distinction(差别)，valid(有效的)，function(功能)，verify(验证)，illustrate(说明)。

## Slide 26
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
2．缩短(略)词的大量采用
采用的缩短词有以下几种。
(1)缩略词的首部(front clipping), 如telephone=phone, university=varsity, helicopter=copter，etc．
(2)缩略词的尾部(back clipping)，如advertisement=ad，debutante=deb，modern=mod，professional=pro，exposition=expo，memorandum=memo，etc．
(3)缩略词的首尾部，如influenza=flu，detective=tec，refrigerator=fridge，etc．
(4)首字母缩略词，如V. O. A. =Voice of America，IOC=International Olympic Committee，WTO=World Trade Organization，CAD=Computer Aided Design，NATO=Noah Atlantic Treaty Organization，CAE=Computer Aided Engineering，CAM=Computer Aided Manufacture，etc．

## Slide 27
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
3．约定的专业术语
在科技英语中大量出现专业术语，专业术语语义较固定，翻译也是固定表达方式，如TCP／IP(Transmission Control Protocol／Internet Protocol，传输控制协议／国际网协议)，relay(继电器)，interface(计算机通信接口)，point-to-point(点对点)，topology(拓扑学)，HTML(Hypertext Markup Language，超文本标识语言)，HTTP(Hypertext Transfer Protocol，超文本传输协议)，LAN(Local Area Network，局域网)，Modem(调制解调器)，aerodynamics(空气动力学)，cybernetics(控制论)，precision(精度)，vector(向量或矢量)，matrix(矩阵)，prototype(原型，样机)，state-of-the-art(工艺水平)，detect(探测，检测)，fault(故障)，hydraulic system(液压系统)，NC(Numerical Control，数控)，milling(铣，磨)，feed(进给量)，machine tool(机床)，feedback(反馈)，hardness(硬度)，coolant(冷却液)，roughness(粗糙度)，sensor(传感器)，integration(集成，综合)，pulse train(脉冲序列)，patent(专利)，poly-phase(多相的)，transformer(变压器)，integrate circuit(集成电路)。

## Slide 28
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
Distribution Automation Increases Reliability

## Slide 29
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
The Long Island Lighting Co. (LILCO) provides service to over a million customers via 750 plus distribution feeders, comprised, mainly, of overhead lines. These feeders are subject to the usual storm-related problems involving damage due to thunderstorms, lightning, tree contact, ice storms and hurricanes. Compared with other New York State electric utilities, on average, LILCO provides the fastest restoration, although customers have in the past experienced more frequent sustained interruptions.
长岛照明公司凭借 750 条附加配电线路，主要是高架线路，向100多万用电单位提供供电服务。这些供电线路易受到与暴风雨有关问题的侵扰，包括雷暴雨、闪电、树挂线、暴风雪、飓风。虽然用户常受到长时间的停电干扰，但与纽约其他电力公司相比，一般来讲，这家公司恢复供电时间最快。

## Slide 30
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
An analysis of customer outages determined that about 78% of interruptions were due to faults on main three-phase lines. A fault on the main line would cause, on average, 2000 customers to lose power. In order to reduce these outages, the company has instituted reliability programmes that include trimming trees, installing lightning arresters, installing covered wire and replacing obsolete armless insulators. These programmes reduced outages, but were not sufficient to reach the desired level of service continuity. To further improve reliability, LILCO has installed an advanced distribution automation system, developed jointly by LILCO and Harris Distributed Automation Products, Calgary, Alberta, Canada. This system isolates faults and restores non-damaged portions of the main line circuit based on real-time parameters of voltage, current, breaker status and supervisor-controlled switch positions. Since this project was initiated in 1993, more than 240, 000 customers have avoided a sustained interruption of service.

## Slide 31
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
在用户断电分析中，测出78％断电的原因是由三相线路上的故障造成的。平均每次主干线路故障将导致2000个用户停电。为了减少这些故障造成断电次数，公司制定出完善可靠的方案，包括树木剪修、安装避雷器、避雷线以及替换老化的、失去绝缘性的绝缘子。这些方案的出台减少了停电次数，但还不能达到连续供电的理想水平。为进一步提高可靠性，LIL 公司安装了先进的配电自动控制系统，该系统是由LIL公司与加拿大加尔伯达省卡加立市的哈里森配电自动化生产厂家共同开发的。该套系统是根据电压、电流、开关情况、监控开关状态的实时参数来隔离故障，并恢复主干线路中未受破坏部分的电压。自该系统在 1993 年被引用以来， 24 万多用户免去了困扰已久的断电干扰。

## Slide 32
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
In the early 1970s, LILCO installed over 400 pole-mounted switches with radio controls. This equipment which included a mix of medium voltage vacuum switches and current sensors reduced outage duration but had little impact on reducing outage frequency. The Autosectionalizing phase required the development of a remote terminal unit with local intelligence that could detect permanent load-side faults and open a motor-operated switch prior to the substation breaker locking out. The Harris DART RTU was selected for this operation, providing transducerless A. C inputs that would directly connect to the existing sensors. In addition, the DART has a patented fault detection algorithm, which was developed and tested by S &• C Electric CO., Chicago, Illinois, U. S. This fault detection scheme can detect three levels of overcurrent, including overcurrent with no loss of voltage, overcurrent with a successful breaker trip reclose and overcurrent with a breaker lockout.

## Slide 33
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
早在20世纪70年代，LIL公司就在电杆上安装了400多个无线电控制开关，这种开关包括中性介质的电压真空开关电流互感器，用以减少停电持续时间，但对停电次数的减少作用不大。自动区域性断电需要一个带有本地智能性的遥控数据终端，用于测出永久负荷端故障，并在变电站出现故障之前，打开电动机控制开关。为达到这样的操作程序，选用了哈里森DART 遥控数据终端。该系统能够在没有发送器的情况下，直接向各传感器输人交流信号。此外 DART 公司还拥有故障探测系统，此项技术已获专利，该系统是由美国伊利诺斯州芝加哥S&C电器公司生产和测试的。它能测出三种过电流等级，包括无电压损耗的过电流、一次性断路跳闸关闭的过电流和断路器闭锁的过电流。

## Slide 34
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
Building upon the fault detection scheme, Harris developed an advanced RTU application, known as the "Smart Switch" or "Autosectionalizer.” This advanced application requires no communications network or relay coordination study to be implemented. Integration of the Autosectionalizers to the 400 existing switches was completed in April of 1996. In addition, LILCO has installed over 350 S & CSCADAmate switches with Autosectionalizer capability. These 750 Autosectonalizing switches enable LILCO to reduce by 25% the number of customers affected by main line faults, amounting to 240,000 customers avoiding a sustained outage in the last 18 months.
当设立故障检测系统后，哈里森公司又开发了一种称为“ SMART " （灵敏的）开关或自动断路器的先进RTU系统，这种先进设备的使用不需要通信网络或继电器配合，把自动断路器接在400个现有开关上。该项任务是在1996年4月正式完成的。另外LIL公司还安装有350个具有自动切断性能的S陇SCADA型开关。这750个故障自动切断开关，使得LIL公司减少了25％的用户再受主三相故障造成的停电影响。共有24万用户在长达一半的时间内免去了持续断电的干扰。

## Slide 35
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
The second stage of the project involved the installation of a Harris PC-based SCADA system along with setting up communications linked with the Autosectionalizing switches, which gave the operators remote indication and control of switches. The Harris PC SCADA provides, on a three-phase basis, voltage, current, power factor, load profiles and other real-time values for optimizing the use of the distribution system. After evaluating several communication mediums, LILCO selected Microwave Data System (MDS) spread spectrum radio network. The MDS radio incorporates unlicensed frequency hopping spread spectrum technology. Using the MDS system, LILCO installed 750 radios and established 90% communications coverage in just under nine months.

## Slide 36
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
第二阶段的项目包括装配以PC为基础的哈里森 SCADA 系统和设立故障自动切断开关通信装置，它们可使操作者对开关实行远距离监视和控制。哈里森PC SCADA系统以三相电为基础，提供电压、电流、功率因数、负载外形以及其他实时数值，以期达到充分发挥这种配电系统的优势。在对一些通信手段进行了一番评估后，LIL公司选用了微波数据系统扩频通信网络。这种微波数据系统还混入了自由频段的扩频跳频技术。由于使用微波数据系统，LIL公司安装了750个无线电台，在几个月的时间内通信覆盖面达90％。

## Slide 37
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
The third stage of the project required the development of an advanced algorithm for the automatic restoration of power reaching the non-faulted feeder zones. This algorithm was written to run on the Harris D-200, which serves as the front end processor for communications with the RTUs.
第三个阶段的任务要求生产一种自动恢复到无故障供电线路的先进系统。论述自动恢复系统要涉及到哈里森D-200，它作为前端处理器用于与 RTUS 保持通信联系。

## Slide 38
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
The Harris D-200 receives information from the Autosectionalizing switches reporting loss of voltage and fault location. In addition, the Harris D-200 receives substation breaker status and loading from the affected circuit as well as information from the adjacent tie circuit. Finally, based on real-time voltage, load, breaker status, switch positions and safety interlocks, the algorithm calculates and reports corrective measures to restore service. The autorestoration algorithm is designed to restore up to 12 feeders simultaneously and will support as many as seven switches arranged in an open loop arrangement. In addition, the operators can set the level of automation for each circuit loop. The levels include;
哈里森D-200从自动切断开关处获得信息，它提供断电信息。另外，哈里森D-200还获取变电站断路器情况和受影响线路的负荷以及邻近线路信息。之后，依照实时电压、负载、断路器情况、开关位置和安全闭锁情况，该系统经过计算，报告出恢复供电的正确方案。设计这种自动恢复系统能同时恢复 12 条供电线路，还可支持多达七个装在开环线路上的开关。此外，操作者能为每一条回路设置自动化等级。这些等级包括：

## Slide 39
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
(1) The manual. The PC SCADA system will not issue a recommendation to restore service. The operators have full supervisory control and indication of switches.
(2) Operator Acknowledgement. The Harris D-200 will determine the faulted zone and then based on real-time information will issue to the PC SCADA a simulation screen and the switching steps required to restore service. If the operator agrees with the algorithm's recommendation, the operator "issues an acknowledgment" enabling the PC SCADA to perform the necessary switching steps. A failure of any switching step aborts the restoration and places the circuit loop into manual.
手动模式：PC SCADA系统不发出恢复供电指令，操作人员可对开关起到全面监控和提示作用。
操作者指令模式：哈里森D-200确定故障范围，然后根据实时信息给PC SCADA呈现一个仿真屏幕以及所需恢复供电的操作步骤。如果操作人员同意系统指令，操作者就发出指令，使PC SCADA 执行必要的操作步骤。任何启动环节的失灵，都会阻碍恢复供电，从而使线路转人手动模式。

## Slide 40
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
(3) Full Automation. Based on the algorithm the faulted zone is determined and the switching is automatically performed to restore the non-faulted zones. All automatic switching steps are based on real-time information, and operator procedures (interlocks) prevent the energizing of work areas. No operator intervention is required.
全自动模式：确立故障范围，继而自动执行起动，恢复到无故障线路的供电。一切自动环节都是按实时信息数据来确定的。因而，操作者工作过程（联锁）阻止工作人员操作，即不需要操作人员的干预。

## Slide 41
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
On April 30, 1996, LILCO received a patent for the advanced restoration algorithm. While many utilities are using supervisory switching to isolate faults, most use operator remote control to restore service. This procedure is time consuming and inefficient, particularly during storm conditions when multiple faulted circuits occur.
1996年4月30日，LIL公司获得这一先进的供电恢复系统的专利。但是许多公司仍采用监控开关隔离故障，而且大多数采用操作员远程控制来恢复供电。这一程序耗时而且效率不高，特别是在暴风雪天气，多处出现线路带故障的时候更是如此。

## Slide 42
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
New words and phrases
hurricane ['hʌrikən ] n. 飓风; 旋风; 风暴
restoration [,restə'reiʃən] n. 回复到原处或原状; 恢复; 修复, 整修
sustained [sə'steind] adj. 持久的;经久不衰的
interruption [intə'rʌpʃən] n. 停止，中断
outage ['autidʒ] n. 停机，断电
reliability [ri,laiə'biləti] n. 可靠性
arrester [ə'restə] n. 捕拿者;止动器;避雷装置
obsolete ['ɔbsəli:t] adj. 不再使用的; 过时的
parameter [pə'ræmitə] n. 参量; 参数.
initiate [i'niʃieit] v.创立；引进
sensor ['sensə] n. 传感器；灵敏元件
transducer [træns'dju:sə] n. 转换器；传感器

## Slide 43
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
patent ['peitnt] adj. 有专利的, 受专利权保护的
algorithm ['ælgəriðəm] n. 规则系统演段
integration [,inti'ɡreiʃən ] n. 综合，集成，同化
Profile ['prəufail] n. 侧面；外形
optimize ['ɔptimaiz] v. 使优化；乐观对待
spectrum ['spektrəm] n. 光谱，频谱；范围，幅度
incorporate [in'kɔ:pəreit] vt. 合并，使并入
unlicensed [,ʌn'laisənst] adj. 没有执照的，未经当局许可的，未经注册的
hop [hɔp] v. 跳；弹跳
adjacent [ə'dʒeisnt] adj. 毗连的; 接近的; 相接触的
interlock [,intə'lɔk] v. 连接;连锁;互锁
simultaneously [,siməl'teinjəsli] adj. 同时，一起
acknowledgement [ək'nɔlidʒmənt] n. 承认，确认，感谢

## Slide 44
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
simulation [,simju'leiʃən] n. 模拟，仿真
abort [ə'bɔ:t] v. 中止;夭折
intervention [,intə'venʃən] n. 介入，干涉，干预
be subject to 遭受
lightning arrester 避雷装置
obsolete armless insulator 过期无防护的绝缘器
real-time parameter 实时参数
a sustained interruption of service 持续断电
reduced outage duration 减少断电时间
a permanent load-side fault 永久负荷侧面故障
Alberta 加尔伯达 （国家地名）
RTU（a Remote Terminal Unit） 远端电源设备

## Slide 45
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
SCADA（ Supervisory Control And Data Acquisition） 监控数据探测
to reach the desired level of service continuity 达到理想的持续供电标准
a three-phase basis 三相基础
power factor 功率因素
spectrum radio network 波谱无线电网络
communication coverage 通信覆盖面
autorestoration algorithm 主动恢复数字系统装置
non-faulted feeder zones 无故障供电范围
autosectionalizing switches 主动分段开关
substation breaker status 变电站断路器状况
the adjacent tie circuit 临近线路

## Slide 46
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
safety interlock 安全连锁
circuit loop 电流回路
full supervisory control 全自动监控
algorithm's recommendation 数字系统指令
operator procedure 操作者程序
multiple faulted circuits 多故障线路
MDS（Microwave Data System） 微波数据系统

## Slide 47
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
Exercises
Ⅰ. Answer the following questions according to the text．
1. What causes the service interruption in most cases?
2. What’s the function of the RTU application, known as the "Smart Switch" developed by Harris?
3. How many levels of automation can we set for each circuit loop when Harris D-200 is used? And what are they?

## Slide 48
Electric Power System Monitoring
自动化专业英语
Unit 9 Electric Power System Monitoring
II．Translate the following phrases and expressions．
1. lightning arrester
2. a sustained interruption of service
3. a permanent load-side fault
4. multiple faulted circuits
5. full supervisory control
6. circuit loop
7. autosectionalizing switches
8. RTU（a Remote Terminal Unit）
9. real-time parameter
10. a three-phase basis
Ex. II.
1. 避雷装置
2. 持续断电
3. 永久负荷侧面故障
4. 多故障线路
5. 全自动监控
6. 电流回路
7. 主动分段开关
8. 远端电源设备
9. 实时参数
10. 三相基础

## Slide 49
Thank You!