## Slide 1: Unit 4
Operational Amplifier

## Slide 2
Translation
Reading more
Translating skills
Text
Operational Amplifier
自动化专业英语

## Slide 3
Operational Amplifier
自动化专业英语

## Slide 4
The operational amplifier is the most important basic building block of all linear circuits.
It has a wide range of applications in such fields as analogue signal operations, amplification, filtering waveforms, producing linear and non-linear signals handling, etc.
第4单元 运算放大器
运算放大器是所有线性电路中最重要的基本器件。其应用十分广泛，包括模拟信号的运算、放大、滤波、产生或进行各种线性或非线性的处理等等。
自动化专业英语

## Slide 5
The term “operational amplifier” was originally applied to high gain amplifiers operating down to zero frequency which were used in analogue computers to perform certain mathematical operations.
These high gain amplifiers are now used for a wide variety of applications, but the name “operational amplifiers” or “op—amp” is normally used even though no mathematical operations are involved.
运算放大器这一术语最早适用于下限频率可低到零赫兹的高增益放大器。它可用于模拟计算机中执行某些数学运算。高增益的放大器现在己广泛应用于各个方面，早就远远超出了数值运算的范围，但通常仍称之为运算放大器或OP-AMP。
自动化专业英语

## Slide 6
The early operational amplifiers employed discrete components, but it is now much more convenient to employ an integrated circuit.
The circuit designers are not generally interested in the internal components of an integrated circuit，but only in the performance of the unit as a whole.
Therefore, the symbol in Fig.4-1 is used to denote the amplifier. It can be seen that there are two inputs, one output and connections to the positive and negative supply lines.
早期的运算放大器采用分立元件，但现在使用集成电路就更加方便了。电路设计者通常对集成电路的内部元件不感兴趣，只关心作为一个整体的单元性能。所以图4-1所示的符号用来表示运算放大器。由图可以看出，运算放大器有两个输入端，一个输出端以及正、负电源端子。
自动化专业英语

## Slide 7
If the inverting input is made slightly more positive，the output will become more negative，this is why the name “inverting” is given to this input.
If, however, the non-inverting input is made more positive，the output will also become more positive.
假如反向输入端正电压略微增加一点，那么输出负电压将变得更强，这就是之所以称这个输入端为“反向输入端”的原因。然而，假如同相输入端电压正向增大，输出端正电压也将变得更强。
自动化专业英语

## Slide 8
Type 741 device is one of the best known general purpose operational amplifiers and is also one of the cheapest of all linear integrated circuits.
The device is actually available in a number of different packages. Readers will usually find the type of 741 shown in Fig 4-2. This type of package is known as the 8 pin dual-in-line.
741型器件是众所周知的通用运算放大器之一，也是所有的线性集成电路中最廉价的一种。这种器件实际上具有很多不同的封装形式。图4-2所示的741型器件是最常见的，这种封装形式为8管脚双列直插式。
自动化专业英语

## Slide 9
A basic circuit of a 741 inverting amplifier is shown in Fig 4-3. The input signal is fed to the inverting input of the 741 via R1 and therefore the output is inverted in phase with respect to the input.
Operational amplifiers are designed to have a very high input impedance. The input currents of the 741 circuit are therefore very small. As the inverting input is virtually at ground potential，the current which flows through R1 is equal to the input voltage ui divided by R3.
Similarly，the current flowing through R3 is –u0 / R3. where u0 is the output voltage. These two currents are almost equal，thus the voltage gain of circuit is equal to the resistor values
G =
741反相放大器的基本电路如图4-3所示。输入信号经R1加在741器件的反相输入端，因此输出信号与输入信号的相位相反。
运算放大器被设计成具有很高的输入阻抗，所以741的净输入电流很小。因此反相输入端虚短，流过R1的电流等于ui除以R3，同样流经R3的电流等于-u0/R3，其中u0是输出电压。这两个电流几乎相等，因此电路的电压增益等于电阻值：

## Slide 10: New words and phrases
operational [,ɔpə'reiʃənəl] adj. 操作的；运作的经营的
variety [və'raiəti] n. 种类；多样；杂耍变化；多种
discrete [dis'kri:t] adj. 离散的，不连续的n. 分立元件；独立部件
filter [filtə] vi. 慢慢传开；滤过 n. 滤波器；筛选vt. 过滤；渗透
filtering ['filtəriŋ] v. 过滤，滤除（filter的ing形式）
integrate ['intiɡreit] vt. 使……成整体vi. 求积分；成为一体adj. 整合的
denote [di'nəut] vt. 表示；指示；意指
gain [ɡein] n. 收获；增益；利润vt. 获得；赚到 vi. 获利；增加
respect [ri'spekt] n. 尊敬；方面；vt. 尊敬，尊重；遵守
自动化专业英语

## Slide 11
virtually ['və:tʃuəli] adv. 事实上，几乎；实质上
invert [in'və:t] a. 转化的 v. 反转，颠倒 [计算机] 反置
package ['pækidʒ] n. 程序包管壳；套装软件vt. 将……包装；打包
pin [pin] n. 大头针；钉；管脚；琐碎物vt. 钉住；将……用针别住
impedance [im'pi:dəns] n. [电] 全电阻；阻抗
be known as 被称为……
in line adv. 成一直线；有秩序；协调 adj. 联机的
自动化专业英语

## Slide 12: Technical Terms
operational amplifier 运算放大器
inverting input 反向输入端
non-inverting input 同向输入端
8 pin dual-in line 8管脚双列直插式
自动化专业英语

## Slide 13: Language points
1. The term“operational amplifier”was originally applied to high gain amplifiers operating down to zero frequency which were used in analogue computers to perform certain mathematical operations.
运算放大器这一术语最早适用于下限频率可低到零赫兹的高增益放大器，它可用于模拟计算机中执行某些数学运算。
句中which引导定语从句，修饰前面的high gain amplifiers，因定语从句并未直接跟在所修饰的先行词后，语法上叫作分隔定语。而定语从句中的to perform certain mathematical operations为动词不定式短语，作目的状语。perform 表示“执行；完成；演奏”，又如：
A series of microcomputer instruction which perform a specific limited task. 执行某一特定有限任务的一系列微机指令。
自动化专业英语

## Slide 14
2．a variety of 种种；各种各样的……；不同种类
1）Here is the network to collect a variety of tools to publish does not limit what type of release can be here.
版块介绍:这里主要是网络搜集来的各种工具公布不限制，什么类型的都可以在这里发布。
2）She offered a variety of excuses.
她提出了各种各样的借口。
3）Accordingly, the Company can provide a variety of products and cheaper prices.
因此，本公司能够提供的产品多种多样，价格便宜。
4）Specifications complete, is the piston ring manufacturing industries in a variety of more complete.
产品规格齐全，是活塞环制造行业中品种较为齐全的一家。
自动化专业英语

## Slide 15
3．If, however, the non-inverting input is made more positive，the output will also become more positive.
然而，如果同相输入端电压正向增大，输出端正电压也将变得更强。
句中the non-inverting input表示“同相输入端”，又如：
nverting input impedance is the same as for the inverting amplifier of Figure 1 and the non-inverting input impedance is the sum of R3 and R4.
反相放大部分的输入阻抗和反相放大器的计算方法相同。同相放大部分的输入阻抗为R3、R4之和。
自动化专业英语

## Slide 16
4. inverting反相；反转 <> non-inverting非反相；不反转
1) A is the non-inverting receiver input/driver output, and B is the inverting receiver input/driver output.
A是正相接收器输入/驱动器输出，B是反相接收器输入/驱动器输出。
2) The dynamic bulk biasing technique is utilized to increase the switching speed of inverting circuits such that the delays of the inverting and non-inverting circuit is very close.
我们利用动态偏压的方式加快反相动态电路转态速度，使得反相与非反相电路的运作速度极为相近。
自动化专业英语

## Slide 17
5. be known as 被称为……；被认为是；以……著称
1) You want to be known as a go-getter who gets the job done well.
你希望人们认为你是一个能把事情做好的“富有进取心的人”。
2) It will be known as the supply chain management process logistics management.
人们将上述过程的管理称之为供应链物流管理。
3) In addition to the unknown or ignorance, human beings seem omnipotent manufacturing，they seem to be known as "manufacturing without limit.
除了未知或无知，人世间似乎无所不能制造，似乎人类可以号称"制造无极限"。
自动化专业英语

## Slide 18
6．with respect to 表示“关于；至于” 例如：
1）With respect to the simulation of the smoke evaluation during a fire, most fire models give the smoke mass density as a result.
关于火灾发生时对于浓烟估算之模拟，大部分的火灾模式是以烟质量密度作为模拟结果。
2）Does my friend see computer matters with respect to dizziness and constitution?
我的朋友看见电脑就头晕和体质有关系么?
自动化专业英语

## Slide 19
3）With respect to data, to change its form or location; to perform arithmetic, logic, or transfer operations with it.
对于数据而言,改变其形式或存储位置,对它执行算术运算、逻辑运算或转移操作。
4）Are the switch mainframe and cards compatible with other equipment in the system with respect to triggering, controls, and connections?
开关主机和插卡是否兼容系统中的其它设备，以实现触发、控制及连接？
自动化专业英语

## Slide 20
7．impedance [im'pi:dəns] n. [电] 全电阻；阻抗
1）To determine if this is the case, first measure a low impedance voltage source through the channel.
为了确定是否发生了这种情况，可以首先通过该通道测量一个较低阻抗的电压源。
2）There is a lot more to good amplifier performance than output impedance.
除了输出阻抗外，还有很多因素才能构成一部好的放大器。
3）When choosing a card to switch high impedance voltage, make sure the card has a low offset current.
在选择切换高阻电压的开关卡时，请确保开关卡具有低偏移电流。
自动化专业英语

## Slide 21: Exercises
I. Answer the following questions according to the text.
Why is the name “operational amplifier” given?
2. Can you draw the circuit symbol of an operational amplifier? Please do.
3. What are the applications of operational amplifiers?
自动化专业英语
It were used in analogue computers to perform certain mathematical operations.
It has a wide range of applications in such fields as analogue signal operations, amplification, filtering waveforms, producing linear and non-linear signals handling, etc.

## Slide 22
1. 滤波 2. 运算放大器
3．输入阻抗 4. 正、负电源端
5．反相输入端虚短 6. 作为一个整体的单元性能
7．8管脚双列直插式集成块 8. 执行各种线性和非线性处理
II. Translate the following phrases and expressions .
filtering waveforms
operational amplifier
自动化专业英语
the input impedence
the positive and negative supply lines
the inverting input is virtually at ground potential
the performance of the unit as a whole
the 8 pin dual-in—line integrated block
performing linear and non-linear signals handling

## Slide 23
The role of a program is to deliver user’s intention to a computer.
2. The best way to access WWW is with a very fast Web browser(浏览器).
3． To turn on an NPN bipolar transistor，the base must be more positive than the emitter.
4. It is necessary for a multimedia system to support a variety of media types．
Ⅲ．Translate the following sentences，paying more attention to the uses of the underlined parts．
程序的作用是将用户的意愿传递给电脑。
最好的方法是以非常快的浏览器去访问万维网。
开通一个NPN双极晶体管,基极一定比发射极电压更高。
自动化专业英语
多媒体系统来支持多种媒体类型是必要的 。

## Slide 24
Amplifiers are necessary in many types of electronic equipment such as radios，oscilloscopes and record players. Often it is a small alternating voltage that has to be amplified. A junction transistor in the common-emitter mode can act as a voltage amplifier if a suitable resistor, called the load，is connected in the collector circuit.
IV. Translate the following passage．
放大器在诸如收音机、示波器和录放机等许多电子设备中是必要的。它经常有一种小的交变电压需要放大。在共发射极模式中的一个结型晶体管，如果称为负载的合适的电阻器连接到集电极回路上可以作为一种电压放大器。
自动化专业英语

## Slide 25
The small alternating voltage, the input ui is applied to the base-emitter circuit and causes small changes of base current which produces large changes in the collector current flowing through the load. The load converts these current changes into voltage changes which form the alternating output voltage uo
把小的交流电压ui 加到基射回路，引起基极电流产生小的变化，从而导致流经负载的集电极电流发生大的变化，负载将电流变化转变成电压变化，就形成了交流输出电压uo。
自动化专业英语

## Slide 26
在翻译过程中，由于英汉两种语言的表达方式不同，不能逐词对译。原文中有些词在译文中须要转换词性，才能使译文通顺流畅。词性转换的几种情况如下：
Translating Skills
词性转换
自动化专业英语

## Slide 27
自动化专业英语
一、英语动词、形容词、副词译成汉语名词
1. Telecommunications means so much in modern life that without it our modern life would be impossible. 电信在现代生活中意义重大，没有它就不可能有我们现在的生活。
2. The cutting tools must be strong, tough, hard and wear resistant.
刀具必须有足够的强度，韧性，硬度，而且耐磨。
3. Dynamics is divided into statics and kinetics, the former treating of forces in equilibrium, the latter of the relation of force to motion.
力学分为静力学和动力学：前者研究平衡力，后者研究力和运动的关系。
4. The image must be dimensionally correct.
图形的尺寸必须正确。

## Slide 28
二、英语名词、介词、形容词、副词译成汉语动词
1. Substitution of manual finishing is one example of HSM application. 替代手工精加工是高速加工应用的一个例子。
2. Scientists are confident that all matter is indestructible.
科学家们深信一切物质是不灭的。
3. In any machine input work equals output work plus work done against friction.
任何机器的输入功，都等于输出功加上克服摩擦所做的功。
4. Open the valve to let air in. 打开阀门，让空气进入。
自动化专业英语

## Slide 29
三、英语的名词、副词和动词译成汉语形容词
1. This wave guide tube is chiefly characterized by its simplicity of structure.
这种波导管的主要特点是结构简单。
2. They said that such knowledge is needed before they can develop a successful early warning system for earthquakes.
他们说，这只是对他们要发明的一种有效的地震早期警报是必要的。
自动化专业英语

## Slide 30
四、英语形容词、名词译成汉语副词
1. With slight repairs the television transmitters can be used.
只要少加修理，这台视频发射机就可使用。
2. A continuous increase in the temperature of a gas confined in a container will lead to a continuous increase in the internal pressure within the gas.
不断提高密封容器内气体的温度，会使气体的内压力不断增大。
自动化专业英语

## Slide 31
自动化专业英语
74LS373
74164时序图
Registers

## Slide 32
Oscillator
A unit that generates a signal is called an oscillator. Electrical oscillators are widely used in radio and television transmitters and receivers, in signal generators，oscilloscopes and computers, to produce A. C. with waveforms which may be sinusoidal，square，sawtooth etc. and with frequency from a few hertz up to millions of hertz1.
Reading More
振荡器
产生信号的电路被称为振荡器。振荡器广泛应用在射频及视频发射机和接收机、信号发生器、示波器和计算机中，以产生正弦波、方形波、锯齿波等交流波形，其频率从几赫兹到数百万赫兹。
自动化专业英语

## Slide 33
Therefore, oscillators may be described in one of two ways in terms of the type of signal waveform generated: sinusoidal oscillators and relaxation oscillators. A sinusoidal oscillator generates a signal having a sine waveform；a relaxation oscillator generates a signal that is usually of square waveform. Sinusoidal oscillators are widely used in radio communication for carrier generation and in many of the test instruments used with such systems. Relaxation oscillators are used as pulse generators in television and radar systems，in digital systems and in test instruments.
因此，依据产生波形的不同将振荡器分为两类：正弦波振荡器和张驰振荡器。正弦波振荡器产生正弦波形的信号，而张驰振荡器通常产生方波信号。正弦波振荡器广泛用于无线电通信中产生载波，而且在许多测试仪器中使用该载波系统。张驰振荡器在电视及雷达系统、数字系统和测试仪器中用作脉冲发生器。
自动化专业英语

## Slide 34
Oscillators generally consist of all amplifier and some type of feedback：the output signal is fed back to the input of the amplifier. The frequency-determining elements may be a tuned inductance-capacitance circuit or a vibrating crystal. Crystal controlled oscillators offer the highest precision and stability. Oscillators are used to produce audio and radio signals for a wide variety of purposes.
振荡器通常包括放大器和某些类型的反馈系统（反馈是指将输出信号送回到放大器的输入端）。频率确定元件可以是电感—电容调谐电路或振荡晶体。晶体控制振荡器的精确度和稳定性非常高。振荡器多用于产生音频及射频信号。
自动化专业英语

## Slide 35
For example，simple audio-frequency oscillators are used in modern push-button telephones to transmit data to the central telephone station for dialing. Audio tones generated by oscillators are also found in alarm clocks, radios，electronic organs, computers, and warning systems. High-frequency oscillators are used in communications equipment to provide tuning and signal-detection2 functions. Radio and television stations use precise high-frequency oscillators to produce transmitting frequencies.
劈如，用于现代按键电话中的简单音频振荡器能把数据传送到需要拨号的任意电话站。由振荡器产生的音频声音还用于时钟警报、无线电通信、电子风琴、计算机和警报系统。高频振荡器被用在通信设备中实现调谐和检波功能。广播电台和电视台应用精密的高频振荡器产生发射频率。
自动化专业英语

## Slide 36
oscillator ['ɔ:sileitə]n. 动摇不定的人，犹豫的人【物理学】振荡器
transmitter [trænz'mitə] n. 发射机，发报机；传达人
receiver [ri'si:və] n. 接收器；接受者；收信机；收款员，接待者
generator ['dʒenəreitə] n. 发电机；发生器
sinusoid ['sainəsɔid] n. 正弦曲线 (sinusoidal adj. 正弦曲线的)
relaxation [,ri:læk'seiʒən] n. 放松；缓和；消遣
vibrating ['vaibreitiŋ] adj. 振动的 n. 振动（vibrate的ing形式）
New words and phrases
自动化专业英语

## Slide 37
crystal ['kristəl] n. 水晶；晶体；水晶饰品 adj. 水晶的；透明的
precision [pri'siʒən] n. 精确；精密度adj. 精密的，精确的
audio ['ɔ:diəu] adj. 声音的；音频的，声频的
tone [təun] n. 音调；语气；色调vt. 用某种调子说 vi. 颜色调和
tuning ['tju:niŋ] n. [无] 调谐；调音，起弦；协调一致；起音，定音
organ ['ɔ:ɡən] n. 风琴；器官；机构；管风琴；嗓音
relaxation oscillators 张驰振荡器
carrier generation 载波
自动化专业英语
New words and phrases

## Slide 38
1. What is called an oscillator? Where can oscillators be widely used?
2. How many types of oscillators can be classified? What are they?
3. What are the advantages of crystal controlled oscillators?
Exercises
I．Answer the following questions according to the reading．
自动化专业英语
A unit that generates a signal is called an oscillator. Electrical oscillators are widely used in radio and television transmitters and receivers, in signal generators，oscilloscopes and computers。
Oscillators can be classified by signal waveform into two types, they are sinusoidal oscillators and relaxation oscillators
Crystal oscillators offer the highest precision and stability.

## Slide 39
1. 正弦波振荡器产生正弦波形的信号.
2. 张驰振荡器产生的通常是方波信号。
3. 高频振荡器用于在通信设备中实现调谐和检波功能。
4. 频率确定元件可以是电感-电容调谐电路或晶体振荡器。
II．II. Put the following into English .
A sinusoidal oscillator generates a signal having a sine waveform.
A relaxation oscillator generates a signal that is usually of square waveform.
High-frequency oscillators are used in communications equipment to provide tuning and signal-detection functions.
自动化专业英语
The frequency-determining elements may be a tuned inductance-capacitance circuit or a vibrating crystal.

## Slide 40
振荡器
产生信号的电路被称为振荡器。振荡器广泛应用在射频
及视频发射机和接收机、信号发生器、示波器和计算机中，
以产生正弦波、方形波、锯齿波等交流波形，其频率从几赫
兹到数百万赫兹。
因此，依据产生波形的不同将振荡器分为两类：正弦波
振荡器和张驰振荡器。正弦波振荡器产生正弦波形的信号，
而张驰振荡器通常产生方波信号。正弦波振荡器广泛用于无
线电通信中产生载波，而且在许多测试仪器中使用该载波系
统。张驰振荡器在电视及雷达系统、数字系统和测试仪器中
用作脉冲发生器。
译文：
自动化专业英语

## Slide 41
振荡器通常包括放大器和某些类型的反馈系统
（反馈是指将输出信号送回到放大器的输入端）。频率确定
元件可以是电感—电容调谐电路或振荡晶体。晶体控制振荡
器的精确度和稳定性非常高。振荡器多用于产生音频及射频
信号。劈如，用于现代按键电话中的简单音频振荡器能把数
据传送到需要拨号的任意电话站。由振荡器产生的音频声音
还用于时钟警报、无线电通信、电子风琴、计算机和警报系
统。高频振荡器被用在通信设备中实现调谐和检波功能。广
播电台和电视台应用精密的高频振荡器产生发射频率。
自动化专业英语

## Slide 42
Thank you!