## Slide 1
Unit 10
Fundamental of Single-chip
Microcomputers

## Slide 2
Fundamental of Single-chip microcomputers
Reading more
Translation skills
Text
Translation

## Slide 3
Fundamental of single-chip microprofessors

## Slide 4
Text:
The single-chip microcomputer is the culmination1 of both the development of the digital computer and the integrated circuit, arguably the two most significant of the 20st century [1] .
单片机是数字计算机和集成电路发展中的一个顶峰，而这二者可以说是20世纪的两项最有意义的发明。

## Slide 5
These two types of architecture are found in single-chip microcomputers.
Some employ the split program/data memory of the Harvard architecture, shown in Fig.10-1, others follow the philosophy, widely adopted for general-purpose computers and microcomputers, of making no logical distinction between program and data memory as in the Princeton architecture, shown in Fig.10-2.

## Slide 7
In general terms a single-chip microcomputer is characterized by the incorporation3 of all the units of a computer into a single device, as shown in Fig.10-3.

## Slide 8
1. Read Only Memory (ROM)
ROM is usually for the permanent, non-volatile4 storage of an application program.
Many microcomputers and microcontrollers are intended for high-volume applications and hence the economical manufactures of the devices require that the content of the program memory be committed5 permanently during the manufacture of the chips.
Clearly, this implies a rigorous approach to ROM code development since changes cannot be made after manufacture. This development process may involve emulation6 using a sophisticated development system with a hardware emulation capability as well as the use of powerful software tools.

## Slide 10
2. Random Access Memory (RAM)
RAM is for the storage for working variables and data during program execution. The size of this memory varies with device type but it has the same characterized width (4, 8, 16 bits, etc.) as the processor.
Special function registers, such as a stacker pointer or timer register are often logically incorporated into the RAM rate. It is also common in Harvard type microcomputers to treat the RAM area as a collection of registers;
it is unnecessary to make a distinction between RAM and professor register as is done in the case of a microprocessor system since RAM and registers are not usually physically separated in a microcomputer.

## Slide 11
3. Central Processing Units (CPU)
The CPU is much like that of any microprocessor. Many applications of microcomputers and microcontrollers involve the handling of binary-coded decimal (BCD) data (for numerical displays, for examples);
hence it is common to find that the CPU is well adapted to handling this type of data. It is also common to find good facilities for testing, setting and resetting individual bits of involve the turning on and off of single output lines or the reading of a single line.
3.中央处理器（CPU）
CPU像其他任何微处理器中的一样。微型计算机和微控制器的应用涉及BCD（二进制编码的十进制数）数据的处理（例如用于数值的显示），因此，采用CPU来处理这类数据就很平常了。并发现它也能用于测试/设置/重置单个位，包含对单个输出线的开启和读取。

## Slide 12
4. Parallel input/output
Parallel input and output schemes vary somewhat in different microcomputers; in most cases a mechanism is provided to at least allow some flexibility of choosing which pins are outputs and which are inputs. This may apply to all or some of the ports.
Some I/O lines are suitable for direct interfacing to, for example, fluorescent displays, or can provide sufficient current to make interfacing to other components straight forward. Some devices allow an I/O port to be configured as a system bus to allow off-chip memory and I/O expansion .

## Slide 13
5. Serial Input/Output
Serial communication with terminal devices is a common means of providing a link using a small number of lines.
This sort of communication can also be exploited for interfacing special function chips or linking several microcomputers together.
Both the common asynchronous and synchronous communication schemes require protocols7 that provided framing (start and stop) information.

## Slide 14
6. Timer / counter facilities
Many applications of single-chip microcomputers require accurate evaluation8 of elapsed9 real time.
This can be determined by careful assessment of the execution time of each branch in a program but this rapidly becomes inefficiently for all but the simplest programs.

## Slide 15
The preferred approach is to use a timer circuit that can independently count precise time increments and generated an interrupt after a preset10 time has elapsed.
This type of timer is usually arranged to be preloadable11 with the required count. This timer then decrements12 this value producing an interrupt or setting a flag when the counter reaches zero.

## Slide 16
Better timers then have the ability to automatically reload the initial count value.
This relieves the programmer of the responsibility of reloading the counter and assessing the elapsed time before the timer is restarted, which otherwise would be necessary if continuous precisely time interrupts were required (as in clock, for example).
Sometimes associated with a timer is an event counter. With this facility there is usually a special pin that can drive the counter directly.

## Slide 18
7. Timing components
The clock circuitry of most microcomputer requires only simple timing components. If maximum performance is required, a crystal must be used to ensure the maximum clock frequency is approached but not exceed.
Many clock circuits also work with a resistor and capacitor as low-cost timing components or can be driven from an external source. This latter arrangement is useful if external synchronization13 of the microcomputer is required.

## Slide 19: New words and phrases

## Slide 20
New words and phrases

## Slide 21: Technical Terms

## Slide 22: Language points

## Slide 23
[2]These two types of architecture are found in single-chip microcomputers.
注：这两种结构一种是哈弗结构：内部（外部）ROM和RAM采取独立编址的方式，这种方法能生成双倍独立空间。
将程序指令存储ROM和数据存储RAM分开的存储器结构。程序在执行时CPU首先到程序指令存储器中读取数据，并进行下一步的操作。一般程序指令和数据采用不同的寻址指令而互不干扰。程序指令存储和数据存储分开，可以使指令和数据有不同的数据宽度。
另一种是普林斯顿结构，也称冯·诺依曼结构，是将程序指令存储器和数据存储器合并在一起的存储结构。程序指令存储地址和数据存储地址指向同一个存储器的不同物理位置，因此程序指令和数据的宽度相同。
Language points

## Slide 24
Language points

## Slide 25: Language points
[3] The CPU is much like that of any microprocessor.
CPU 像其他任何微处理器中的一样。

## Slide 26: Language points
[4]some devices allow an I/O port to be configured as a system bus to allow off-chip memory and I/O expension.
notes: "off-chip memory"译为“片外存储”。
第一个“allow”连接了第一个“to”，译为“允许……（干）……”，第二个“to allow”作补语。

## Slide 27: Language points
[5]This can be determined by careful assessment of the execution time of each branch in a program but this rapidly becomes inefficient for all but the simplest programs.
Notes:"in-"表示“否定，与……相反”之意，“inefficients”译为“效率低的，效率差的”。
“all but”译为“几乎，差一点”。

## Slide 28: I．Identify the following to be true（T）or false（F）according to the text.
1. In general terms a single-chip microcomputer is characterized by the incorporation of all the units of a computer into a single device.
2. RAM is usually for the permanent, non-volatile storage of an applications program.
3. ROM is for the storage of working variables and data used during program execution.
4. Serial communication with terminal devices is a common means of providing a link using a small number of lines.
5. Many clock circuits also work with a resistor and capacitor as low-cost timing components or can be driven from an external source.
Ex. I. （T）/（F）/（F）/（T）/（T）

## Slide 29: II．Reading Comprehension
(1) Which of the following are not the feathers of ROM? ____.
A. permanent storage B. Non-volatile storage
C. Can’t be changed after manufacture D. Can be changed at any moment
(2) RAM hasn’t the characterized width of ____.
A. 16 bits B. 8 bits C. 4 bits D. 2 bits
(3) Parallel I/O can’t be used for_____.
A. fluorescent displays B. serial communications
C. interfacing to other components D. I/O expansion
(4) Serial I/O can’t be used for _____.
A. linking with terminal devices B. interfacing special function chips
C. linking several microcomputers together D. connecting with CPU
(5) The timing components consist of the following except_____.
A. Resistors B. capacitors C. Crystals D. Inductance
Ex. II. 1. （D） 2. （D） 3. （B） 4. （D） 5. （D）

## Slide 30
Translating Skills
被动语态的译法
被动语态的翻译准则：
“忠实”
“通顺”
Translating Skills
被动语态的译法

## Slide 31
Translating Skills
翻译方法

## Slide 32
Translating Skills
翻译方法

## Slide 33
Translating Skills
翻译方法

## Slide 34
Translating Skills
翻译方法

## Slide 35
Translating Skills
翻译方法

## Slide 36
chip and chip holder

## Slide 37
Reading More
Translation

## Slide 38
Translation

## Slide 39
Translation

## Slide 40
New words and phrases

## Slide 41
Exercises

## Slide 45: I．Translate the following phrases and expressions．
1. Super-large-scale integrated circuit
2. Dual in-line (DIL) package socket
3. If you need to remove a chip it can be gently prized out of the holder with a small flat-blade screwdriver.
Ex. I.
1. 超大规模集成电路
2. 双列直插插座
3. 如果需要移除芯片，可以使用小型平口螺丝刀轻轻地撬起插座。

## Slide 46
Thank you!