## Slide 1
Unit 3
Integrated Circuit

## Slide 2
Integrated Circuit
Reading more
Translation skills
Text
Translation

## Slide 3
Integrated Circuit

## Slide 4
Text:
Integrated circuit, or IC is a combination of a few interconnected1 circuit elements such as transistors，diodes，capacitors，and resistors produced in a single manufacturing process on one and the same bearing structure，called the substrate2，and intended to perform definite function involved in converting information[1].
集成电路缩写为IC，是几个互相连接的电路元件的组合，比如晶体管、二极管、电容器和电阻器等电路元件的组合。它们组装在同一个基底结构上，同时由一个单独制造过程生产出来的，这个基底结构叫做衬底，集成电路可用于信息转换中执行确定的功能。

## Slide 5
The electrically interconnected components3 that make up [2] an IC are called integrated elements．If an integrated circuit includes only one type of components， such as only diodes or resistors，it is said to be an assembly or set of components．
组成集成电路互相连接的元件称为集成元件。假若集成电路只包含一种类型的元件，例如仅由二极管或电阻器组成，就称为元件组件。

## Slide 6
The principle4 of integrated circuit elements lies in the following．A great number of “set” are produced simultaneously on a wafer．
Each set contains all the components such as transistors，diodes，and resistors which are interconnected with short fine metallic5 stripes deposited6on the wafer surface [3]．They make up an functional7 block．
Each ICs of components is a ready integrated circuit．All ICs are regularly distributed on the wafer8 surface．
电路元件的集成原理如下：首先把许多“组”同时制作在晶片上，每个组包含诸如晶体管、二极管和电阻之类的全部元件，各元件被沉积在晶片表面上的短细金属条互相连接起来，组成一个功能模块。每个元件组都是一个现成的集成电路，所有集成电路都按一定规则分布在晶片表面。

## Slide 7
ICs can be classified by [4] function into two：circuits to be applied in digital systems and those to be applied in linear systems．
The digital ICs are employed mostly in computers，electronic counters，frequency synthesizers9and digital instruments．
And the analog，or linear ICs operate over a continuous range，and include such devices as operational amplifiers．
集成电路按其功能可分为两大类，即用于数字系统的电路和用于线性系统的电路。数字集成电路主要应用于计算机、电子计数器、频率合成器等数字仪器中。模拟或线性集成电路可在连续范围内工作，通常包括诸如运算放大器之类的器件。

## Slide 8
The invention of IC is a great revolution in the electronic industry．
Sharp10 size，weight reduction are possible with these techniques；and more importantly，high reliability，excellent functional performance，low cost and low power dissipation can be achieved．
ICs are widely used in the electronic industry．
集成电路的发明是电子工业的一次伟大革命。利用这种技术，完全可能实现尺寸明显缩小和重量减轻。更重要的是能够获得高度可靠性、优良的工作性能、低成本和低功耗。集成电路广泛应用于电子工业。

## Slide 9: New words and phrases
1.interconnect [intə(:)kə'nekt] vt. 使互相连接, vi. 互相
2. substrate ['sʌbstreit] n. 基质；基片；衬底（等于 substratum）
3. component [kəm'pəunənt] n．成分，元件组件
adj. 组成的，构成的
4. principle ['prinsəpl] n．原理，原则；道义；
本义；根源，源泉
5. metallic [mi'tælik, me-] adj. 金属的，含金属的
n. 金属纤维

## Slide 10
New words and phrases
6.deposit [di'pɔzit] n．堆积物，沉淀物
v．存放，堆积，沉淀
7.functional ['fʌŋkʃənl] adj. 功能的；职能的；函数的
8.wafer ['weifə] n. 圆片，晶片；薄片，干胶片；
vt. 用干胶片封
9.synthesizer ['sinθisaizə] n. 合成者；合成器；合成仪；综合器
10.sharp [ʃa:p] adj. 急剧的；锋利的；强烈的
adv. 锐利地
n. 内行；尖头

## Slide 11: Technical Terms
electronic counter 电子计数器
frequency synthesizer 频率合成器
digital instrument 数字仪器

## Slide 12: Language points
1．Integrated circuit，or IC is a combination．．．to perform definite function involved in converting information．
集成电路缩写为IC，是几个互相连接的电路元件的组合，如晶体管、二极管、电容器和电阻器等电路元件的组合。它们是在同一个基底结构上，同时是在一个单独制造过程中生产出来的。这个基底结构叫做衬底。集成电路可以在信息转换中执行一定的功能。
produced ．．．为过去分词短语作定语，修饰前面的circuit elements，其中的produced与intended to为并列部分；而called the substrate为过去分词短语作定语，修饰前面的the same bearing structure，同时 involved in converting information也是过去分词短语作定语，修饰前面的function。

## Slide 13: Language points
2. intend to打算做……，倾向于……，想要……
e.g. 1） I intend to work in the information services (service) industry, or market sectors. 我意向从事信息服务行业，或者市场销售行业。
2）I intend to give up my present post in order to get a more challenging opportunity. 为了获得一个更有挑战性的工作机会，本人打算放弃目前的职位。
3）I intend to become the master of my own body level dream.
我意愿成为精通我自己身体水平梦想的大师。

## Slide 14
3. make up弥补；组成；形成；化妆；整理；临时编造；重归于好
1）Sky and sea make up of a harmonious picture.
天空和大海构成了一副和谐的画面。
2）These signals make up computer language.
这些信号构成计算机语言。
Language points

## Slide 15
Language points
4．Each set contains all the components such as transistors，diodes，and resistors which are interconnected with short fine metallic stripes deposited on the wafer surface．
每个组包含诸如晶体管、二极管和电阻之类的全部元件，各元件用沉积在晶片表面上的短细金属条互相连接起来。
句中的which are…the wager surface为定语从句，修饰前面的transistors，diodes，and resistors，而定语从句中的deposited on the wafer surface为过去分词短语作定语，修饰前面的metallic stripes。

## Slide 16: Language points
5. be classified by 把……分成
1）Both computerized and manual accounting systems require transactions to be classified by type.
计算机会计系统和手工会计系统都要求交易根据类型被分类。
2） Privilege existed in history in multiple forms, and may be classified by character into three broad categories: economic, political, and cultural.
特权在历史上具有多种形态，按其性质可分为经济特权、政治特权和文化特权三大类。

## Slide 17: Language points
6. dissipation [,disi‘peiʃən] n．消耗，分散
1） related phrases：power dissipation电力分散；功耗energy dissipation消能；能量耗散 generalized dissipation广义耗散 dissipation loss耗散损失，散射损失dissipation function消散函数；散逸函数
2）Features: Low collector saturation voltage, high power dissipation.
特点:饱和压降低，集电极耗散功率高。
3）Backplane heat, dust invasion can be avoided, better heat dissipation effect.
背板散热，可避免灰尘入侵，散热效果更佳。
4）Features: Excellent self-healing, small size, high capacitance, low dissipation and good reliability.特点：具有良好自愈性，体积小，容量大，损耗低，可靠性高。
5）The crust of capacitor made of aluminum, strong rust-less, the capability of heat dissipation is superior to other materials.
选用铝材作为电容器的外壳，坚固不生锈，散热性能优越于其它材料；
6）In these tests, integral energy dissipation system can suppress structural vibration with satisfaction displacement. 试验结果表明:组合耗能体系对位移有良好的减振效果;

## Slide 18: Exercises
Answer the following questions according to the text．
1．What is integrated circuit? What functions can integrated circuits perform?
2. What are called integrated elements?
Integrated circuit is a combination of a few interconnected circuit elements such as transistors，diodes，capacitors，and resistors produced in a single manufacturing process on one and the same bearing structure，called the substrate，and intended to perform definite function involved in converting information.
The electrically interconnected components that make up2 an IC are called integrated elements．

## Slide 19: Exercises
3. Can you describe the principle of integrated circuit elements? Try to present it.
4. How many types can ICs be classified into by function? What are they?
5. Why is the invention of IC a great revolution in the electronic industry?
The principle of integrated circuit elements lies in the following．A great number of “set” are produced simultaneously on a wafer．Each set contains all the components such as transistors，diodes，and resistors which are interconnected with short fine metallic stripes deposited on the wafer surface．They make up an functional block．
ICs can be classified by function into two：circuits to be applied in digital systems and those to be applied in linear systems．
Because sharp size，weight reduction are possible with these techniques；and more importantly，high reliability，excellent functional performance，low cost and low power dissipation can be achieved．

## Slide 20: Exercises
II. Translate the following into English．
电子计数器 2. 频率合成器
3. 低成本和低功耗 4. 在同一个基底结构上
5. 集成电路已广泛应用于电子工业。
electronic counters
frequency synthesizers
low cost and low power dissipation
on one and the same bearing structure
ICs are widely used in the electronic industry．

## Slide 21: Exercises
6．数字集成电路广泛应用于计算机、电子计数器等数字仪器中。
7．集成电路就是把所有的电路元件集成在一块半导体芯片上。
The digital ICs are employed mostly in computers，electronic counters，and digital instruments．
Integrated circuit is a combination of a few interconnected circuit elements on a piece of semiconductor chip.

## Slide 22: Exercises
III．Translate the following short passage into Chinese．
An integrated circuit looks like nothing more than a tiny chip of metal，perhaps one-half of a centimeter on a side，and not much thicker than a sheet of paper．It is so small that if it fell on the floor, it could be easily swept up with the dust．Although it is very small，it represents the most highly skilled technology at every step of its manufacture．At today’s level of development，it might comprise more than ten thousand separate electronic elements including elements of many different functions，such as diodes，transistors，capacitors and resistors．

## Slide 23: Exercises
Key: 集成电路看起来只不过是一个微小的金属片，或许一
个侧面只有二分之一厘米宽，比一张纸厚不了多少。芯片这么
小，如果它掉到地板上，就很容易跟垃圾一起扫走。尽管它很
小，芯片的生产过程却应用了当代最高电子技能技术。到今天
的发展水平，芯片可能包含一万多单独的电子元件（这些电子
元件，诸如二极管，晶体管，电容器和电阻器等）所具有的许
多不同功能。

## Slide 24
Translating Skills
引申译法
Translating Skills

## Slide 25
Translating Skills
英汉两种语言在表达上有很大差别。翻译时，有些词或词组不能直接搬用词典中的释义，若生搬硬套，会使译文生硬晦涩，难以看懂，甚至造成误解。所以，要在弄清原文内涵的基础上，根据上下文的逻辑关系和汉语的搭配习惯，对词义加以引申。若遇到有关专业方面的内容，必须选用专业方面的术语。引申后的词义能更确切地表达原文意义。例如：

## Slide 26
Translating Skills
1. However, colors can give more force to the form of the product.
欠佳译法：然而，色彩能给予产品更多的力量。
引申译法：然而，色彩能使产品外形增添美感。
2. Power plugs are male electrical connectors that fit into female electrical sockets.
欠佳译法：电源插头是雄性连接器适配雌性连接器。
引申译法：电源插头可以插入电源插座。

## Slide 27
Translating Skills
3 There is a wide area of performance duplication between numerical control and automatics.
引申译法：数控和自动化机床有很多相同的性能。
4. High-speed grinding does not know this disadvantage.
引申译法: 高速磨床不存在这个缺点。
5. The charge current depends upon the technology and capacity of the battery being charged.
引申译法：充电电流的大小根据充电技术和电池容量的不同而不同。

## Slide 28
DIGITAL CIRCUIT

## Slide 29
Reading More
Translation
Digital Circuit
The phrase digital “electronics” is used to describe those circuit systems which primarily operate with the use of only two different voltage levels or two other binary states．The two different states by which digital circuits operate may be of several forms．They can，in the most simple form，consist of the opening and closing of a switch．In this case，the closed-switch state can be represented by 1 and the open-switch state by 0．

## Slide 30
Translation
A very common method of digital operation is achieved by using voltage pulses．The presence of a positive pulse can be represented by 1 and the absence of a pulse by 0．With a square-wave signal，the positive pulses can represent 1 and the negative pulses can represent 0．

## Slide 31
Translation
Integrated circuits containing many transistors are most commonly used as switching devices in digital electronics logic gates．The three basic types of digital logic gates are the AND gate，the OR gate，and the NOT gate (as shown in Fig．3-1)．The operation of an AND gate is mathematically expressed by the equation A×B = C．This can be read as “input A and input B equals output C”．The operation of an OR gate is often expressed by the equation A+B = C．This can be read as “either input A or input B (or both) equals output C”．An important function of NOT gate is to produce signal inversion or an output signal that is opposite in nature to the input signal．Any logic function can be performed by the three basic gates that have been described．Even in a large scale digital system，such as a computer，control，or digital-communication system，there are only a few basic operations，which must be performed．The three basic types of digital logic gates and the flip-flop are the four circuits most commonly employed in such systems．

## Slide 32
Translation
&
A
B
C
A×B=C
≥1
A
B
C
A+B=C
1
A
C
○
A = C
Fig．3-1 Digital Logic Gates

## Slide 33
New words and phrases
primarily ['praimərəli] adv. 主要地，根本上；首先；最初的
binary ['bainəri] adj. 二元的，二态的；二进制的
pulse [pʌls] n. 脉搏；脉冲vt. 使跳动vi. 跳动，脉跳
represent [repri'zent] vt. vi. 表现；描绘；代表；回忆；再赠送
nature ['neitʃə] n. 自然；性质；种类；本性
inversion [in'və:ʃən] n. 倒置；倒转；反向反转

## Slide 34
New words and phrases
scale [skeil] n.刻度，衡量，数值范围 v. 依比例决定；攀登
flip-flop ['flipflɔp] n. 触发器；啪嗒啪嗒的响声vt. 使翻转；使突然转变
the closed-switch state 开关闭合状态
the open-switch state 开关断开状态
logic gates [计算机] 逻辑闸；逻辑门电路库；逻辑门
and gate 和门；与门；与电路
binary arithmetic 二进制算术

## Slide 35
Exercises
I．Write T (True) or F (False) after the following statements according to the text.
1．The closed-switch state can be represented by 1 and the open-switch state can be represented by 0．
2． A very common method of digital operation is achieved by using current pulses．
3．Integrated circuits containing many transistors are most commonly used as switching devices in digital electronics logic gates．
4．The three basic types of digital logic gates are the AND gate，the OR gate，and the NOT gate．
5．An important function of NOT gate is to produce signal inversion or an input signal that is opposite in nature to the output signal．
6．The three basic types of digital logic gates and the flip-flop are the four circuits most commonly employed in such systems．
（T）
(F)
（T）
（T）
（F）
（T）

## Slide 36
Exercises
Ⅱ．Translate the flowing into Chinese．
Digital signals and circuits are the vast and important subject．Digital signals are binary in nature taking on values in one of two well-defined ranges．The set of basic operations that be performed on digital signals is quite small．The behavior of any digital system, (up to and including the most sophisticated digital computer) can be represented by appropriate combinations of digital variables and the digital operations from this small set．
We concerned with digital system variables that take on only two values (binary variables)．We conventionally denote these values as “0” or “1”，and then use a special set of rules called Boolean algebra to summarize the various ways in which digital variables can be combined．This algebra and much of the notation are adopted directly from mathematical logic．Thus, “logic variable” or “logic operation” are commonly used in place of digital variable，or digital operation．
(KEY)

## Slide 37
Exercises
数字信号和电路是广阔且重要的课题。数字信号在本质上是一个二进制的数，表示两个具有严格定义阈值范围的电压。能够对数字信号进行的运算相当少。任何数字系统（直至包括最先进的数字计算机）的行为都可以由数字变量和来自该集合的数字运算进行适当地组合来表示。
我们关注的数字系统变量，只有两个示值（二进制变量）。我们通常把这些数值用“0”或“1”来表示，然后使用一个特殊的规则即布尔代数来概括用各种方式组合起来的数字变量。其代数和符号，有许多是直接从数学逻辑吸收来的。因此，“逻辑变量”或“逻辑运算”通常可以用来取代数字变量或数字运算。

## Slide 38
数字电路
“数字电子技术”这一术语是用于叙述只用两种不同电压电平或两种不同的二进制状态进行工作的电路系统。数字电路用于工作的两种不同状态有几种表现形式。最简单的一种形式是由开关的断开和闭合状态组成的。在这种情况下，开关闭合状态用1表示，其断开状态用0表示。
Translation

## Slide 39
Translation
很普通的数字运算方法是用电压脉冲完成的。有正脉冲存在用1表示，没有正脉冲存在用0表示。若用方波信号，正脉冲可代表1，负脉冲代表0。

## Slide 40
含有许多晶体管的集成电路主要用作电子数字逻辑门中的开关器件。有三种基本逻辑门，分别是与门、或门和非门(如图3-1所示)。与门运算用数学等式可表示为A×B=C，读作“输入A和输入B等于输出C”。或门运算常用方程A+B=C表示，读作“或输入A或输人B(或两者)等于输出C”。非门的重要功能是产生反向信号，也就是产生与输入信号性质相反的输出信号。任何一种逻辑功能都可用上述三种基本逻辑门电路来完成。即使是在大规模数字系统中，比如计算机系统、控制系统或数字通信系统中，需要进行的基本运算也只有这几种。三种基本类型的数字逻辑门和触发器是这些系统中最常用的四种电路。
译文

## Slide 41
Thank you!