## Slide 1
Unit 7
Power System

## Slide 2
Unit 7 Power System
自动化专业英语
Power System
Translation
Reading More
Translating skills
Text
Power System

## Slide 3
Power system
Unit 7 Power System
自动化专业英语
Power System

## Slide 4
Unit 7 Power System
自动化专业英语
Power System
Electricity is only one of many forms of energy used in industry, homes, businesses, and transportation. It has many desirable features: it is clean (particularly at the point of use), convenient, relatively easy to transfer from point of source to point of use, and highly flexible in its use. In some cases it is irreplaceable energy source.
The power system consists of power sources, called generating plants (or generators), power end users, called loads, and a transmission and distribution network that connects them. Most commonly the generating plants convert energy from fossil or nuclear fuels, or from falling water, into electrical energy.
电能是工业、家庭、商业和交通的最主要的能源之一。电源有许多令人满意的特点：清洁（尤其从使用的角度来看），方便，很容易从生产地传输到需要用的地方，而且适用性广。有时它是一种不可替代的能源。
电能系统由能源（称为发电站或发电厂）、终端用户（称为负载）和一个连接发电站与负载的输电配电网络组成。最常见的发电站是把燃料或核能或落水的势能转换成电能。

## Slide 5
Unit 7 Power System
自动化专业英语
Power System
FOSSIL-FUEL PLANT
In a fossil-fuel plant, coal, oil, or natural gas is burned in a furnace. The combustion produced hot water, which is converted to steam, and the steam drives a turbine, which is mechanically coupled to an electric generator. In brief, the operation of the plant is as follows: Coal is taken from storage and fed to a pulverizer (or mill), mixed with preheated air, and blown into the furnace, where it is burned.
在燃料电厂中，用煤、油或天然气烧锅炉，通过燃烧把锅炉中的水加热变成蒸汽，蒸汽推动汽轮机，汽轮机与发电机有机械上耦合（即汽轮机转动带动发电机转动）。简单地说，电厂的运行是这样的：煤从仓库取出，送入一个粉碎机（或磨粉机），与预先加热的空气混合后喷入锅炉，在锅炉中燃烧。

## Slide 6
Unit 7 Power System
自动化专业英语
Power System
The furnace contains a complex of tubes and drums, called a boiler, through which water is pumped and the temperature of the water rises in the process until the water evaporates into steam. The steam passes on to the turbine, while the combustion gases (flue gases) are passed through mechanical and electrostatic precipitators, which remove upward of 99% of the solid particles (ash) before being released to the chimney or stack.
锅炉中有复杂的管道和鼓状的设备，称为沸腾器，水泵把水压入沸腾器，在沸腾器中水温度上升并蒸发成为蒸汽。蒸汽通过汽轮机，而燃烧后的气体（流动的气体）通过机械和静电沉淀器，把超过99％的固体粒子（灰）除去，然后通过烟囱排放出去。

## Slide 7
Unit 7 Power System
自动化专业英语
Power System
The unit just described, with pulverized coal, air, and water as an input and steam as a useful output, is variously called a steam-generating unit, or furnace, or boiler.
When the combustion process is under consideration, the term furnace is usually used, while the term boiler is more frequently used when the water-steam cycle is under consideration.
The steam, at a typical pressure of 3500 psia and a temperature of 1050 F, is supplied through control and stop (shutoff) valves to the steam turbine.
The control valve permits the output of the turbine-generator unit (or turbogenerator) to be varied by adjusting steam flow. The stop valve has a protective function.
刚才提到的，输入煤粉、空气和水，输出有用的蒸汽的单元有很多个名称：蒸汽发生器、锅炉或沸腾器。当考虑到燃烧的功能时，就用锅炉这个名称，而沸腾器则更经常地用于考虑水-蒸汽循环的时候。典型的每平方英寸3 500 磅的压力、1 050华氏度的蒸汽通过控制和制动阀送到汽轮机中。控制阀通过调节蒸汽流控制汽轮机-发电机的输出，制动阀起保护作用。

## Slide 8
Unit 7 Power System
自动化专业英语
Power System
The turbine turns the rotors of the electric generator in whose stator are embedded three (phase) windings.
In the process mechanical power from the turbine drive is converted to three-phase alternating current at voltages in the range from 11 to 30 kV line to line at a frequency of 60Hz in the United States.
The voltage is usually "stepped up" by transformers for efficient transmission to remote load centres.
汽轮机带动发电机的转子，发电机的定子上嵌入三相绕组。在这个过程中汽轮机的机械能转换成三相交流电，在美国，定子输出有效值为11～30 kV、频率为60 Hz的线电压。这三相电压一般要通过升压变压器升压，再通过输电网传到遥远的负载中心。

## Slide 9
Unit 7 Power System
自动化专业英语
Power System
TRANSMISSION & DISTRIBUTION SYSTEM
The sources of electric power described in the preceding sections are usually interconnected by a transmission system or network that distributes the power to the various load points or load centres.
The generator voltages are in the range of 11 to 30 kV. Higher generator voltages are difficult to obtain because of insulation problems in the narrow confines of the generator stator. Transformers are then used to step up the voltages to the range of 110~765 kV for transmission. The voltages refer to voltages from line to line. Near the loads, the transmission voltage is stepped down to the voltages used by loads.
输配电系统
上节所描述的电源通常连接到输电系统或输电网，把电能送到各个负载点或负载中心。
发电机（输出的）电压为11～30kV，因为发电机的定子大小有限，要获得更高的输出电压在绝缘方面还有问题不能解决。然后用变压器升压到110～765kV，以便于传输，这里的电压都是指线电压（有效值）。到负载端，电压再（通过变压器）降到负载所要求的电压。

## Slide 10
Unit 7 Power System
自动化专业英语
Power System
The loads referred to here represent bulk loads, such as the distribution system of a town, city, or large industrial plant. Such distribution systems provide power at various voltage levels.
Large industrial consumers or railroads might accept power directly at voltage levels of 23 to 138 kV; they would then step down the voltages further.
Smaller industrial or commercial consumers typically accept power at voltage levels of 4.16 to 34.5 kV. Residential consumers normally receive single phase power from pole-mounted distribution transformers at voltage levels of 120/240 V.
负载指的是大负载，如一个城镇或一个大工厂的配电网。这样的配电系统可以提供各种电压级别的电源。大工厂的用户或轨道负载可以直接用23～138kV的高电压电源供电，然后再把电压（根据需要）进一步降压。小工厂或商业用户典型的供电电压为4.16～34.5kV，居民区一般用配电变压器的某一相单相供电，供电电压为120/240V。

## Slide 11
Unit 7 Power System
自动化专业英语
Power System
Transmission circuits may be built either underground or overhead.
Underground cables are used mostly in urban areas where acquisition of overhead rights of way is costly or not possible. They are also used for transmission under rivers, lakes and bays.
Overhead transmission is used otherwise because, for a given voltage level, overhead conductors are much less expensive than underground cables.
输电线路可以是架空线路或埋在地下。在城市中常用地下电缆，因为城市里铺设架空线路成本比较大或者是不可能实现的。地下电缆也常埋在河底下、湖底下和海湾底下。其他地方则用架空线，因为对一个指定的电压级，架空线的成本远低于地下电缆。

## Slide 12
Unit 7 Power System
自动化专业英语
Power System
The distribution system transports the power from the transmission system to the customer.
The distribution systems are typically radial because networked systems are more expensive.
The equipment associated with the distribution system includes the substation transformers connected to the transmission systems, the distribution lines from the transformers to the customers and the protection and control equipment between the transformer and the customer.
The protection equipment includes lightning protectors, circuit breakers and fuses. The control equipment includes voltage regulators, capacitors, and demand side management equipment.
配电网把来自输电网的电能传送给用户。配电网一般是点辐射式系统，因为网络式系统成本比较高。配电网上连接的设备包括与输电网相连接的配电变压器，从配电变压器到用户的配电线路和变压器与用户之间的保护控制设备。保护设备包括避雷保护、断路器和熔断器。控制设备包括电压调节器、电容和必要的辅助操作设备。

## Slide 13
Unit 7 Power System
自动化专业英语
Power System
One reason for using high transmission-line voltages is to improve energy transmission efficiency. Since the power transmitted is equal to the product of the current, the voltage and the cosine of the phase difference ( ), the same amount of power can be transmitted with a lower current by increasing the voltage.
用高压传输的原因是可以提高能量输送的效率。因为所传输的有功功率等于电流、电压和功率因数（相位差必的余弦）的积，通过增加电压、减少电流可以传输相同的功率。

## Slide 14
为什么要减少传输电流呢？事实是流过导体的有功功率损耗是导体电阻和电流平方的乘积，用公式表示，这就意味着在给定的导线上传输一定的有功功率时，如果电流加倍，则功率损耗是原来的4倍。所以用高电压在电网上传输大量的功率（通常是几百千伏）是很有好处的。
用高压传输的另一个原因是增加传输网的稳定性。
Why a lower current is needed for transmission? The fact is that the power losses in a conductor are a product of the square of the current and the resistance of the conductor, described by the formula .
This means that when transmitting a fixed power on a given wire, if the current is doubled, the power loss will be four times greater. Therefore it is advantageous when transmitting large amounts of power to distribute the power with high voltages.
Another reason for higher voltages is the enhancement of stability.

## Slide 15
Unit 7 Power System
自动化专业英语
Power System
New words and phrases
flexible ['fleksəbəl] adj. 易弯曲的，柔韧的；灵活的，可变通的
irreplaceable [,iri'pleisəbl] adj. 不可替代的，独一无二的
transmission [trænz'miʃən] n. 传输，播送，变速器，传递的信息
distribution [,distri'bju:ʃən] n. 分发，分配；散布，分布
furnace ['fə:nis] n. 熔炉，火炉
combustion [kəm'bʌstʃən] n. 燃烧
turbine ['tə:bain] n. 涡轮机，汽轮机
schematic [ski:'mætik] adj. 扼要的，图解的
pulverizer ['pʌlvə,raizə] n. 粉碎机，喷雾器，粉碎者
evaporate [i'væpəreit] v.蒸发，挥发；消失；使蒸发，使挥发
valves [vælv] n. 阀，活门；(心脏的)瓣膜，(乐器的)活瓣

## Slide 16
insulation [,insju'leiʃən; ,insə'leiʃən] n. 隔离，孤立，绝缘
residential [,rezi'denʃəl] adj. 提供住宿的；居住的；住宅的
fus [fju:z] n. 保险丝，引线，导火线
enhancement [in'hɑ:nsmənt] n. 增强;提高，放大
stability [stə'biliti] n. 稳定，稳固
convert into 把…转换成
be coupled to 与…连接起来
In brief 简言之，简单地说
in the process 在进行中
step up 增加某事物; 促进某事物
step down 逐渐缩小，降低
Unit 7 Power System
自动化专业英语
Power System

## Slide 17
Unit 7 Power System
自动化专业英语
Power System
Technical Terms
fossil-fuel plant 燃料电厂
mechanical and electrostatic precipitators 机械和静电沉淀器
steam-generating unit蒸汽发生器
three-phase alternating current 三相交流电
transmission and distribution system输配电系统
lightning protectors 避雷保护
circuit breakers 断路器
voltage regulators 电压调节器

## Slide 18
Unit 7 Power System
自动化专业英语
Power System
Language points
1. The combustion produced hot water, which is converted to steam, and the steam drives a turbine, which is mechanically coupled to an electric generator.
通过燃烧把锅炉中的水加热变成蒸汽，蒸汽推动汽轮机，汽轮机与发电机有机械上耦合（即汽轮机转动带动发电机转动）。
句中，通过并列连词“and”连结两个独立的句子。两个句子里面的“which”均引导一个非限定性定语从句，且都在定语从句中担当主语成分。

## Slide 19
Unit 7 Power System
自动化专业英语
Power System
2. In brief, the operation of the plant is as follows: Coal is taken from storage and fed to a pulverizer (or mill), mixed with preheated air, and blown into the furnace, where it is burned.
简单地说，电厂的运行是这样的：煤从仓库取出，送入一个粉碎机（或磨粉机），与预先加热的空气混合后喷入锅炉，在锅炉中燃烧。
主句中，“taken from storage”， “fed to a pulverizer”, “mixed with preheated air”, “blown into the furnace”, 是几个并列的相同的句子成分，“where”引导一个定语从句，where作为关系副词，在定语从句中作状语。
3. The turbine turns the rotors of the electric generator in whose stator are embedded three (phase) windings.
汽轮机带动发电机的转子，发电机的定子上嵌入三相绕组。
句中，“whose”作关系代词在定语从句中作定语，修饰跟在它后面的名词stator，相当于The turbine turns the rotors of the electric generator and the stator of the electric generator are embedded three (phase) windings.

## Slide 20
Unit 7 Power System
自动化专业英语
Power System
4. The generator voltages are in the range of 11 to 30 kV higher generator voltages are difficult to obtain because of insulation problems in the narrow confines of the generator stator.
发电机（输出的）电压为11～30kV，因为发电机的定子大小有限，要获得更高的输出电压在绝缘方面还有问题不能解决。“In the range of”含义是：在 ... 范围内。
5. Transmission circuits may be built either underground or overhead. Underground cables are used mostly in urban areas where acquisition of overhead rights of way is costly or not possible.
输电线路可以是架空线路或埋在地下。
either...or...用于表示在两个可能性中任择其一。例如:
either French or Spanish
或法国的或西班牙的
You can either write or phone to request a copy.
既可以写信也可以打电话索取一本.

## Slide 21
Unit 7 Power System
自动化专业英语
Power System
6. The fact is that the power losses in a conductor are a product of the square of the current and the resistance of the conductor
事实是流过导体的有功功率损耗是导体电阻和电流平方的乘积.
句中，that 引导了一个表语从句，连词that在句中本身没有意义，只起连结作用，不担当句子成分。

## Slide 22
Unit 7 Power System
自动化专业英语
Power System
Exercises
Ⅰ．Answer the following questions according to the text．
1. What does a power system consist of?
2. How does a fossil-fuel plant work?
3. What do the control equipment and the protection equipment include?
4. Why do we have to use high transmission-line voltage?

## Slide 23
Unit 7 Power System
自动化专业英语
Power System
II．Judge the following are true (T) or false (F)
according to the text．
1. Near the loads, the transmission voltage is stepped up to the voltages
used by loads. ( )
2. The transmission voltages refer to voltages from line to line. ( )
3. The distribution systems are typically loop system because networked
systems are more expensive. ( )
4. One reason for using high transmission-line voltages is to improve energy
transmission efficiency. ( )
5. when transmitting a fixed power on a given wire, if the current is doubled,
the power loss will be two times as well. ( )
Ex. II. 1.F 2.T 3.F 4.T 5.F

## Slide 24
Unit 7 Power System
自动化专业英语
Power System
Ⅲ. Translate the following expressions into English.
1. transmission and distribution network
2. Transmission circuit
3. The power system
4. transmission and distribution network
5. fossil-fuel plant
6. three-phase alternating current
7. transmission &distribution system
8. lightning protectors
9. circuit breakers
10. voltage regulators
1. 输电配电网络
2. 输电线路
3. 电能系统
4. 输电配电网络
5. 燃料电厂
6. 三相交流电
7. 输配电系统
8. 避雷保护
9. 断路器
10. 电压调节器

## Slide 25
Unit 7 Power System
自动化专业英语
Power System
Ex. IV.
1. A step-down transformer has a turns ratio less than 1.
2. The UN plays an irreplaceable role in maintaining world peace, achieving universal security and promoting common development.
3. They could not agree about the distribution of the profits.
4. The stability of bearing materials is of utmost importance to the stability of the gyro.
IV. Put the following sentences into English:
1. 降压变压器的匝数比小于1。
2. 联合国在维护世界和平、实现普遍安全、促进共同发展方面具有不可替代的作用。
3.他们对于利润的分配意见不一致。
4. 轴承材料的稳定性对陀螺仪(gyro)的稳定性是极为重要的。

## Slide 26
Unit 7 Power System
自动化专业英语
Power System
Translating Skills
数量增减的翻译
英语中倍数的表达与汉语的倍数表达有一定差别，在翻译时要注意。
一、数量增加的翻译
(一)下列情况可译为“比……增加了n倍”。
1．n times+形容词(或副词)＋than
Some electronic computers can do calculations 500,000 times faster than any
person can．
有些电子计算机的运算速度比人快500000倍。
This dam is twice longer than that one．
这座大坝比那座坝长2倍。
(或译为：这座大坝的长度是那座坝的3倍。)
2．表示增加的动词＋by＋n times (或n﹪)
The output of the steel has increased by three times．
钢产量增加了3倍。
The number of the students in school has increased bv 15﹪．
在校学生的数量增加了15﹪。

## Slide 27
Unit 7 Power System
自动化专业英语
Power System
(二)下列情况可理解为“比…增加n－1倍”、“是…的n倍”。
1．n times＋as＋adj./adv. (原级)＋as，可译为“增加了n－1倍”。
This bridge is five times as long as that one．
这座桥比那座长4倍。(或译为：这座桥的长度是那座的5倍。)
2．n times＋the size (volume，length，width等)＋of，译为“增加了
n－1倍”或“是原来的n倍”。
This room is four times the size of that one．
这个房间比那个大3倍。(或译为：这个房间的大小是那个的4倍。)
3．表示增加的动词＋n -fold，可译为“增加了n－1倍”
This will increase its strength tenfold．
这将使其强度增加9倍。

## Slide 28
Unit 7 Power System
自动化专业英语
Power System
(三)在“increase by n times”的句型中，译为“增加了n倍”。例如：
In this case both the pulse spacing and the group length are increased by eight times．
在这种情况下，脉冲间隔及脉冲组长度均增加了8倍。
The population has increased by 300,000．
人口增加了三十万。
但by与动词multiply连用或用于by a factor of n times时表示增加了
n－1。例如：
The sales of industrial electronic products have been multiplied by seven times since 1996．
1996年来，工业电子产品的销售量已增加了6倍。
The speed has exceeded the average speed by a factor of 2.3.
该速度已经超过了平均速度的1.3倍。

## Slide 29
Unit 7 Power System
自动化专业英语
Power System
二、数量减少的翻译
下列情况下可理解为：
1．表示减少的动词＋n times，译为：减少为原来的1/n。
Switching time of the new-type transistor is shortened four times．
新型晶体管的开关时间缩短为原来的1/4。
2．n times＋as＋adj./adv．(原级)＋as，可译为：是……的1/n．
This shop is five times as small as that one．
这个车间相当于那个车间的1/5。
3．表示减少的动词＋by a factor of n times，译为：减少了n－1/n或减少为(到)原来的1/n。
The loss of electricity was reduced by a factor of three．
电的损耗减少到原来的1/3。
4．a n times (n-fold)＋reduction，译为：减少了n－1/n。
The length of the plastic pipe is a three times reduction over that of the metal one.
这个塑料管的长度比那根金属管的长度缩短了2/3。
The principal advantage of the products is a twofold reduction in weight．
这些产品的主要优点是重量减轻了1/2。

## Slide 30
Unit 7 Power System
自动化专业英语
Power System
Transformers

## Slide 31
Unit 7 Power System
自动化专业英语
Power System
Transformers come in many sizes. Some power transformers are as big as a house. Electronic transformers, on the other hand, can be as small as a cube of sugar. All transformers have at least one coil; most have two although they may have many more.
The usual purpose of transformers is to change the level of voltage. But sometimes they are used to isolate a load from the power source.
变压器大小不一。有的变压器像房子一样大。而电子变压器可能小如糖块。所有的变压器至少有一只线圈；大多数变压器具有两个或两个以上的线圈。
通常使用变压器的目的是改变电压等级，但有时也用于隔离电源和负荷。

## Slide 32
Unit 7 Power System
自动化专业英语
Power System
TYPES OF TRANSFORMERS
Standard power transformers have two coils. These coils are labeled PRIMARY and SECONDARY. The primary coil is the one connected to the source. The secondary is the one connected to the load. There is no electrical connection between the primary and secondary. The secondary gets its voltage by induction.
The only place where you will see a STEP-UP transformer is at the generating station. Typically, electricity is generated at 13, 800 volts. It is stepped up to 345, 000 volts for transmission. The next stop is the substation where it is stepped down to distribution levels, around 15, 000 volts. Large substation transformers have cooling fins to keep them from overheating. Other transformers are located near points where the electric power is used.
变压器的类型
标准电力变压器有两只线圈。这些线圈标记为一次绕组（一次侧）和二次绕组（二次侧）。一次绕组连接电源，二次绕组连接负荷。在一次和二次绕组间没有电的连接。二次绕组通过感应获得电压。
大概只有在发电厂才能见到升压变压器。典型的发电机出口电压为 13800V，升压至345000V用来输送。下一站是变电所，把电压降到配电电压等级，约1500V。大型的变电所变压器具有冷却叶片，以防止变压器过热。有的变压器安装的位置靠近用户。

## Slide 33
Unit 7 Power System
自动化专业英语
Power System
TRANSFORMER CONSTRUCTION
The coils of a transformer are electrically insulated from each other. There is a magnetic link, however. The two coils are wound on the same core. Current in the primary magnetizes the core. This produces a magnetic field in the core. The core field then affects current in both primary and secondary.
There are two main designs for cores:
1. The CORE type has the core inside the windings.
2. The SHELL type has the core outside.
变压器的结构
变压器的线圈之间是绝缘的，但存在磁联系。两只线圈绕在同一个铁芯上。一次绕组电流使铁芯磁化，并在铁芯中产生磁场。铁芯磁场影响一次和二次绕组的电流。
铁芯主要有两种型式：
1．芯型。铁芯在线圈内部。
2．壳型七铁芯在线圈外部。

## Slide 34
Unit 7 Power System
自动化专业英语
Power System
Smaller power transformers are usually of the core type. The very large transformers are of the shell type. There is no difference in their operation, however.
Coils are wound with copper wire. The resistance is kept as low as possible to keep losses low.
小型电力变压器通常为芯型。特大型变压器为壳型，但是在运行时二者并无区别。
线圈用铜线绕成。电阻应尽量小，从而保持低损耗。

## Slide 35
Unit 7 Power System
自动化专业英语
Power System
IDEALIZED TRANSFORMERS
Transformers are very efficient. The losses are often less than 3 percent. This allows us to assume that they are perfect in many computations.
Perfect means that the wire has no resistance. It also means that there are no power losses in the core.
Further, we assume that there is no flux leakage. That is, all of the magnetic flux links all of the turns on each coil.
理想变压器
变压器效率很高，损耗通常低于3％。因此这使我们假定它在计算时是无损耗的。
无损耗意味着线圈没有电阻，并且铁芯中没有能量损耗。进一步可以假定没有漏磁，即所有的磁力线穿过线圈的每一匝。

## Slide 36
Unit 7 Power System
自动化专业英语
Power System
EXCITATION CURRENT
To get an idea of just how small the losses are, we can take a look at the EXCITATION CURRENT. Assume that nothing is connected to the secondary. If you apply rated voltage to the primary, a small current flows. Typically, this excitation current is less than 3 percent of rated current.
Excitation current is made up of two parts. One part is in phase with the voltage. This is the current that supplies the power lost in the core. Core losses are due to EDDY CURRENTS and HYSTERESIS.
励磁电流
欲知损耗的大小，可以看一下励磁电流。假定二次绕组空载，在一次绕组施加额定电压后会产生一较小电流。典型情况是该励磁电流小于额定电流的3％。
励磁电流由两部分组成。一部分与电压同相，该电流供给铁芯中的能量损耗。铁芯损耗的原因是涡流电流和磁滞。

## Slide 37
Unit 7 Power System
自动化专业英语
Power System
Eddy currents circulating in the core result from induction. The core is, after all, a conductor within a changing magnetic field.
Hysteresis loss is caused by the energy used in lining up magnetic domains in the core. The alignment goes on continuously, first in one direction, then in the other.
The other part of the excitation current magnetizes the core. It is this magnetizing current that supplies the "shuttle power". Shuttle power is power stored in the magnetic field and returned to the source twice each cycle. Magnetizing current is quadrature (90 degrees out of phase) with the applied voltage.
涡流电流在铁芯中旋转，产生感应现象，因为铁芯毕竟是变化磁场的导体。
磁滞损耗是由于用来排列铁芯中的磁畴需要能量。这种排列调整是连续不断的，开始是一个方向，然后是另一个方向。
另一部分励磁电流磁化铁芯。磁化电流供给“往复能量”，往复能量就是储存在磁场中的能量，并在每个周期内返回电源两次。磁化电流与所加电压正交（相位差为90°）。

## Slide 38
Unit 7 Power System
自动化专业英语
Power System
New words and phrases
transformer [træns'fɔ:mə] n. 变压器
substation ['sʌbsteiʃn] n. 变电所
fin [fin] n. 散热片
overheat [əuvə'hi:t] vt. 使过热，过热
magnetize ['mægnitaiz] vt. 使磁化; 吸引
winding [waindiŋ] n. 绕组；线圈
idealize [ai'diəlaiz] vt. 使理想化
computation [,kɔmpju:'teiʃn] n. 计算；估计
leakage ['li:kidʒ] n. 漏; 漏损物; 泄漏; 漏损量
excitation [,eksi'teiʃn] n. 激发；励磁；刺激
eddy ['edi] n. 漩涡；涡流

## Slide 39
Unit 7 Power System
自动化专业英语
Power System
hysteresis [,histə'ri:sis] n. 滞后（现象）；滞后作用
domain [də'mein] n. 领域；范围
alignment [ə'lainmənt] n. 定线；准线
shuttle[ʃʌtl] n. 梭形；往复
quadrature ['kwɔdrətʃə] n. 求积；矩；上（下）弦
electronic transformer 电力变压器
step-up transformer 升压变压器
excitation current 励磁电流
in phase with 与……相同
eddy current 涡轮电流
shuttle power 往复能量

## Slide 40
Unit 7 Power System
自动化专业英语
Power System
Exercises
I．Answer the following questions according to the text．
1.What is the usual purpose of transformers?
2. What is the eddy current?
3. What is the Hysteresis loss?

## Slide 41
Unit 7 Power System
自动化专业英语
Power System
II．Translate the following phrases and expressions．
1. 一次绕组
2. 二次绕组
3. 理想变压器
4. 励磁电流
5. 涡流电流
6. 磁滞损耗
Ex. II.
1. the primary coil
2. the secondary coil
3. idealized transformer
4. excitation current
5. eddy current
6. hysteresis loss

## Slide 42
Thank You!