## Slide 1: Unit 5
Multimeters and Oscilloscopes

## Slide 2
Translation
Reading more
Translating skills
Text
Multimeters and Oscilloscopes
自动化专业英语

## Slide 3
Multimeters and Oscilloscopes
自动化专业英语
portable multimeters
dual-trace oscilloscope

## Slide 4
1. Multimeters
A multimeter is a general-purpose meter capable of measuring DC and AC voltage, current, resistance, and in some cases, decibels.
There are two types of meters：analog, using a standard meter movement with a needle (see Fig 5-1(a)), and digital, with an electronic numerical display (see Fig 5-1(b)).
自动化专业英语

## Slide 5
Both types of meters have a positive(+)jack and a common jack(-) for the test leads, a function switch to select DC voltage, AC voltage, DC current, AC current, or ohms and a range switch for accurate readings.
The meters may also have other jacks to measure extended ranges of voltage (1 to 5 kV) and current (up to 10A). There are some variations to the functions used for specific meters．

## Slide 6
Besides the function and range switches (sometimes they are in a single switch), the analog meter may have a polarity switch to facilitate reversing the test leads.
The needle usually has a screw for mechanical adjust to set it to zero and also a zero adjust control to compensate for weakening batteries when measuring resistance．
自动化专业英语

## Slide 7
An analog meter can read positive and negative voltage by simply reversing the test leads or moving the polarity switch．A digital meter usually has an automatic indicator for polarity on its display．

## Slide 8
Meters must be properly connected to a circuit to ensure a correct reading. A voltmeter is always placed across (in parallel) the circuit or component to be measured.
When measuring current, the circuit must be opened and the meter inserted in series with the circuit or component to be measured.
When measuring the resistance of a component in a circuit, the voltage to the circuit must be removed and the meter placed in parallel with the component．
自动化专业英语

## Slide 9
2. The oscilloscope
The oscilloscope (Fig 4-2) is basically a graph-displaying device—it draws a graph of an electrical signal. When the signal inputs into the oscilloscope, an electron beam is created, focused, accelerated, and properly deflected to display the voltage waveforms on the face of a cathode-ray tube (CRT)．
自动化专业英语

## Slide 10
自动化专业英语
In most applications the graph shows how signals change over time：the vertical (Y) axis represents voltage and the horizontal (X) axis represents time.
The amplitude of a voltage waveform on an oscilloscope screen can be determined by counting the number of centimeters (cm)，vertically，from one peak to the other peak of the waveform (Fig 5-3) and the multiplying it by the setting of the volts/cm control.
As an example，if the amplitude was 5cm and the control was set on 1V/cm，the peak-to-peak voltage would be 5V．

## Slide 11
Time can be measured using the horizontal scale of the oscilloscope．Time measurements include measuring the period，pulse width，and frequency．
Frequency is the reciprocal of the period，so once you know the period，the frequency is one divided by the period．

## Slide 12
The frequency of a waveform can be determined by counting the number of centimeters, horizontally, in one cycle of the waveform and the multiplying it by the setting time/cm control.
For example, if the waveform is 4cm long and the control is set at 1ms/cm, the period would be 4ms.The frequency can now be found from the formula :

## Slide 13
f = = = 250Hz
If the control was gone on 100 us/cm, the period would be 400us and the frequency would be 2.5kHz.
A dual-trace oscilloscope is advantageous to show the input signal and output signal of one circuit in the same time, to determine any defects, and indicate phase relationships. The two traces may be placed over each other (superimposed) to indicate better the phase shift between two signals.

## Slide 14: New words and phrases
accelerate [ək'seləreit] vt. 使……加快； vi. 加速；促进；增加
multimeter [mʌl'timitə] n. 万用表，数字万用表，多用电表
oscilloscope [ɔ'siləskəup] n. [物]示波器；示波镜
amplitude ['æmplitju:d] n. 广阔，丰富，振幅
analog ['ænəlɔɡ] n. 类似物；模拟 adj. 有长短针的；模拟的
facilitate [fəsiliteit] vt. 促进；帮助；使容易
insert [in'sə:t, 'insə:t] vt. 插入；嵌入 n. 插入物
deflect [di'flekt] vt. 使偏斜；使转向；使弯曲 vi. 偏斜；转向
multiply [‘mʌltiplai] v. 乘；（使）相乘adv. 多样地adj.多层的
reciprocal [ri'siprəkəl] adj. 相互的；倒数的n. 倒数
beam ['bi:m] n. 梁，（光线的）束，电波 v. 播送
自动化专业英语

## Slide 15
compensate ['kɔmpenseit] v. 偿还，补偿，付报酬
decibel ['desibel] n. 分贝
defect ['di:fekt, di'fekt] n. 缺点，缺陷 vi. 叛变；变节
focus ['fəukəs] n. 焦点;焦距;中心 v.（使）聚焦n. 焦点，焦距
horizontally [hɔ:ri'zɔntli] adv. 水平地
jack [dʒæk] n. 插孔，插座，起重器 vt.（用起重器）抬起
meter ['mi:tə] n. 公尺；仪表；米vt. 用仪表测量vi. 用表计量
needle ['ni:dl] n. 针；指针；针状物；刺激 vi. 缝纫；做针线
period ['piəriəd] n. 周期，期间；课时；月经 adj. 某一时代的
superimposed ['sju:pəim'pəuzd] adj. 上叠的；重迭的；叠加的
vertical ['və:tikəl] adj. 垂直的n. 垂直线
自动化专业英语

## Slide 16: Technical Terms
cathode-ray tube (CRT) 阴极射线显像管
dual-trace oscilloscope 双踪示波器
in parallel with 与……并联
in series with 与……串联
peak-to-peak voltage 电压峰-峰值
phase shift 相位漂移/差别，移相
polarity switch 极性开关
rms voltage 电压有效值
自动化专业英语

## Slide 17: Language points
1.The needle usually has a screw for…adjust control to compensate for weakening batteries when measuring resistance．
另外当测量电阻时一个零点调节控制（钮）用来对电池电压不足时做补偿调节（即保证电阻为0时指针指向零值）。
句中to compensate for weakening batteries 作后置定语。compensate vi. 补偿，赔偿vt. 补偿，赔偿；付报酬
1) related phrases：partially compensate 部分补偿 removal compensate拆迁费 compensate control 补偿控制
2) The price of these products will just compensate the cost of equipment and installation of the line.
你方生产的产品价格将正好补偿我方提供的设备及安装生产线的费用。
自动化专业英语

## Slide 18
2. amplitude ['æmplitju:d] n. 振幅；广阔；丰富，充足
1) related phrases：amplitude resolution幅值分辨率 amplitude detection振幅检波 amplitude modulation 振幅调剂 amplitude locus振幅轨迹
2) Sound waves are measured by their amplitude .
声波是根据其振幅来测量的.
3) This represents successive stages of transfer of amplitude to later lobes.
这代表振幅向后面波瓣传递的相继各阶段。
4) In communications, the amplitude variations of an amplitude modulated carrier wave. 在通信技术中，调幅载波的幅度变化图。
自动化专业英语

## Slide 19
3. deflect [di'flekt] vt. 使偏斜；使转向；使弯曲 vi. 偏斜；转向
1) related phrases：deflect missile 拨档飞弹 deflect arrows御箭术/加强对弓箭伤害的抵御力 deflect from使偏斜于
2) Easy to adjust and simple to deflect.
调偏容易，调整简单。
3) You deflect compliments in the presence of foreign friends.
外国朋友在场时，会把别人的赞美推掉。
4) But analyst Rothenberg says so far, Mr. Obama has been able to deflect some of the partisan criticism.
但是分析家博格说到此为止，奥巴马能够扭转部分党派批评。
自动化专业英语

## Slide 20
4. When the signal inputs into the oscilloscope, an electron beam is created, focused, accelerated, and properly deflected to display the voltage waveforms on the face of a cathode-ray tube (CRT)．
当信号输入到示波器中时，一个电子束被产生、聚焦、加速并适当偏离，在阴极射线管的显示屏上显示电压的波形。
句中to display the voltage waveforms… 作结果状语。focuse: “聚焦； 全神贯注”，又如：
自动化专业英语

## Slide 21
1) Quit dicking around. We have a lot of work to do. You need to stay focuse.
你别再瞎闹了，我们还有很多工作呢，全神贯注吧。
2) ever since the thing is very urgent that needs our priority focuse , we will think about it ahead.
既然这件事情非常紧急，需要我的优先关注，自然我会首先考虑它。
3) "For his part, Senator Obama remained focuse focused on the economy and its impact on the average Americans.
对他来说，奥巴马仍然聚焦于经济和其对于普通美国人的影响。
自动化专业英语

## Slide 22
5. defect ['di:fekt, di'f-, di'fekt] n. 缺点，不足之处vi. 叛变
1) related phrases：defect report缺陷报告design defect设计缺陷 | 事故性缺陷 birth defect先天性缺陷 | 新生儿缺陷 dental defect牙体缺损
2) A defect database that has all these fields built into it is able to sort defect data and make it useful information.
缺陷数据库如果能包含所有以上这些字段，就能够对缺陷数据进行合理的排序，从而变成有用的信息。
3) Subject of right refers to those who suffered injuries from the defect in products, including natural person, legal person and other organizations.
产品责任的权利主体是受到产品缺陷损害的—切受害者，包括自然人、法人和其他组织。
自动化专业英语

## Slide 23
6．The amplitude of a voltage waveform…by counting the number of centimeters (cm)，vertically，from one peak to the other peak of the waveform (Fig 4-3)and the multiplying it by the setting of…
在示波器屏幕上的电压波形的幅度可以通过数出电压波峰与波谷之间纵向距离的厘米值来确定（图4-3），将这厘米值乘上V/cm控制钮的设定值就得到电压的幅度值。
句中from one peak… 作后置定语，修饰centimeters，by counting…and the multiplying it by… 是方式状语，修饰be determined。multiply: vt. 乘；使相乘；使增加；使繁殖 vi.增加；乘 adv. 多样地 adj. 多样的；多层的
1) related phrases：multiply unit乘法部件logical multiply逻辑乘 multiply cloth 多层布，多层织物cross multiply 交叉相乘decimal multiply 十进制乘法
自动化专业英语

## Slide 24
2) The only way on earth to multiply happiness is to divide it.
世界上唯一成倍地增加幸福的办法是与人分享.
3) Their first device could add, subtract, multiply and divide.
他们的第一个计算器能够进行加，减，乘，除。
4) A few seconds of fiddling let scientists and engineers multiply, divide and find square and cube roots.
只要拨弄几秒钟，科学家或工程师就能计算乘除、求出平方根与立方根。
自动化专业英语

## Slide 25: Exercises
I. Answer the following questions according to the text.
1. What can be measured with a multimeter? ?
2. What is the function of a oscilloscope?
自动化专业英语
A multimeter is capable of measuring DC and AC voltage, current, resistance, and in some cases, decibels.
The oscilloscope is basically a graph-displaying device—it draws a graph of an electrical signal.

## Slide 26
3. Do you know the differences between a digital multimeter and an analog meter? Can you describe them?
4. What is the advantage of an dual-trace oscilloscope?
自动化专业英语
An analog multimeter uses a standard meter movement with a needle ,and a digital multimeter is with an electronic numerical display . An analog meter can read positive and negative voltage by simply reversing the test leads or moving the polarity switch．A digital meter usually has an automatic indicator for polarity on its display．
A dual-trace oscilloscope is advantageous to show the input signal and output signal of one circuit in the same time, to determine any defects, and indicate phase relationships.

## Slide 27
1. general-purpose meter 2. reverse the test leads
3. mechanical adjust 4. voltage amplitude
5. dual-trace oscilloscope 6. signal generator
7. analog multimeter 8. phase relationship
9. display the voltage waveform 10. positive voltage
II. Put the following phrases into Chinese.
通用仪表
交换测试笔
自动化专业英语
机械调节
电压幅度
双踪示波器
信号发生器
模拟万用表
相位关系
显示电压波形
正电压

## Slide 28
模拟万用表有一个极性开关，可以很方便交换测试笔的极性。
2. 对特殊的万用表而言，还有一些其他功能的变化。
3. 示波器显示一个电子信号的图像。
Ⅲ．Translate the following sentences into English．
The analog meter may have a polarity switch to facilitate reversing the test leads.
There are some variations to the functions used for specific meters．
The oscilloscope displays/ draws a graph of an electrical signal
自动化专业英语

## Slide 29
4. 双踪示波器具有同时显示输入信号和输出信号的优点。
5. 两路信号的波形重叠在一起能显示输入与输出信号相位的差别。
Ⅲ．Translate the following sentences into English．
A dual-trace oscilloscope is advantageous to show the input signal and output signal of one circuit in the same time.
The two traces may be placed over each other (superimposed) to indicate better the phase shift between two signals.
自动化专业英语

## Slide 30
词的增译就是在译文中增加一些原文中无其形而有其义的词。英语中有时为了避免重复，常省略一些词而不影响全句意义的完整表达，但在汉语译文中省略了这些词，就会使译文意义不明确，不通顺。所以，在某些场合的翻译中增词法是非常必要的。
Translating Skills
增词译法
自动化专业英语

## Slide 31
自动化专业英语
一、用汉语动词补充英语名词、动名词或介词的意义，使译文通顺
1. The world needn’t be afraid of a possible shortage of coal, oil, natural gas or other sources of fuel for the future.
世界无需担心将来可能出现煤、石油、天然气、或其它燃料来源短缺的问题。
2. The molecules get closer and closer with the pressure.
随着压力增加，分子越来越接近。

## Slide 32
二、在表达动作意义的英语名词后增添汉语名词
1. This lack of resistance in very cold metals may become useful in electronic computer.
这种在甚低温中金属没有电阻的现象，可能对电子计算机很有作用。
2. The lower the frequency is, the greater the refraction of a wave will be. 频率越低，波的折射作用就越强。input work equals output work plus work done against friction.
任何机器的输入功，都等于输出功加上克服摩擦所做的功。
4. Open the valve to let air in.
打开阀门，让空气进入.
自动化专业英语

## Slide 33
三、增加表示名词复数的词
1. The moving parts of a machine are often oiled that friction may be greatly reduced.
机器的各个可动部件被润滑油润滑，以便大大减少摩擦。
2. The first electronic computers used vacuum tubes and others components and this made equipment very large and bulky.
第一代电子计算机使用电子管和其他元件， 这使设备又大又笨。
自动化专业英语

## Slide 34
四、增加某些被动语态或动名词中没有具体指出的动作执行者或暗含的逻辑主语
1. The material is said to behave elastically.
我们说，这种材料具有弹性。
2. To explore the moon’s surface, rockets were launched again and again.
为了勘探月球的表面，人们一次又一次的发射火箭。
自动化专业英语

## Slide 35
五、在形容词前加名词
1. According to Newton’s Third Law of Motion action and reaction are equal and opposite.
根据牛顿运动第三规律， 作用力和反作用力是大小相等方向相反的。
2. The washing machine of this type is indeed cheap and fine.
这种类型的洗衣机真是物美价廉。
自动化专业英语

## Slide 36
六、增加表示数量意义的概括性的词，起修饰润色作用
1. The frequency, wavelength and speed of sound are closely related.
声音的频率、波长与速度三者密切相关。
2. A designer must have a good foundation in statics, kinematics dynamics and strength of materials.
一个设计人员必须在静力学、运动学、动力学和材料力学这四个方面有很好的基础。
自动化专业英语

## Slide 37
七、增加使译文语气连贯的词
In general, all the metals are good conductors, with silver the best and copper the second.
一般来说， 金属都是良导体， 其中银最佳， 铜次之。
自动化专业英语

## Slide 38
自动化专业英语
Oscillator
radio transmitter
电视发射机
汽车信号发生器
中频信号发生器
音频振荡器
弛张振荡器电路结构

## Slide 39
How Does an Oscilloscope Work
To better understand the oscilloscope controls, you need to know a little more about how oscilloscopes display a signal.
When you connect an oscilloscope probe to a circuit, the voltage signal travels through the probe to the vertical system of the oscilloscope. Fig. 5-4 is a simple block diagram that shows how an analog oscilloscope displays a measured signal.
Reading More
示波器是如何工作的
为更好地掌握示波器的操作方法，你需要知道
示波器是怎样显示信号（图像）的。
当把示波器的探头与一个电路相连接时，电压
信号通过探头送到示波器的垂直系统，图5-4 是
一个简单的线框图，说明一个模拟示波器是怎
样显示一个测量信号的。
自动化专业英语

## Slide 40
Depending on how you set the vertical scale (volts/div
control), an attenuator reduces the signal voltage or an
amplifier increases the signal voltage.
Next, the signal travels directly to the vertical deflection
plates of the cathode ray tube (CRT). Voltage applied to these
deflection plates causes a glowing dot to move. (An electron
beam hitting phosphor inside the CRT creates the glowing
dot.) A positive voltage causes the dot to move up while a
negative voltage causes the dot to move down.
当设定了垂直单位（电压／单位格）时，就确定了是用衰减器还是用放大器（把输入信号转换成适当幅度的电压信号）。
接着，信号直接传到阴极射线管的垂直偏离
板上，施加到这些偏离板的电压大小导致发光
点的移动（一个电子束撞击阴极射线管内部磷
（荧光物质）上产生光点），一个正电压使光
点向上移动，而一个负电压使光点向下移动。
自动化专业英语

## Slide 41
The signal also travels to the trigger system to start or trigger a “horizontal sweep”. Horizontal sweep is a term referring to the action of the horizontal system causing the glowing dot to move across the screen. Triggering the horizontal system causes the horizontal time base to move the glowing dot across the screen from left to right within a specific time interval. Many sweeps in rapid sequence cause the movement of the glowing dot to blend into a solid line. At higher speeds, the dot may sweep across the screen up to 500,000 times each second.
同时信号也输入到触发系统去启动或触发一个“水平扫描”，水平扫描是一个专业术语，是指水平系统的作用导致光点沿着屏幕（水平）移动，水平系统的触发导致水平扫描发生器驱动光点在一个指定的时间间隔内从屏幕的左边移到右边。快速有序多次扫描导致这些光点的移动混合成一条实线。以高速扫描的示波器，每秒中扫过屏幕的光点可能高达 50 万次。
自动化专业英语

## Slide 42
自动化专业英语
Fig. 5-4 analog oscilloscope block diagram

## Slide 43
Together, the horizontal sweeping action and the vertical deflection action traces a graph of the signal on the screen. The trigger is necessary to stabilize a repeating signal. It ensures that the sweep begins at the same point of a repeating signal, resulting in a clear picture as shown in Fig. 5-5.
水平扫描和垂直偏离的作用合在一起就在屏幕上形成了信号的图像轨迹。为了稳定一个重复（周期性）的信号，触发器是必要的，它保证在重复（周期性）信号的同（相位）点开始扫描，进而产生一个清晰的图像，如图5-5 所示。
自动化专业英语

## Slide 44
自动化专业英语
Fig. 5-5 triggering stabilizes a repeating waveform

## Slide 45
In conclusion, to use an analog oscilloscope, you need to
adjust three basic settings to accommodate an incoming
signal:
1.The attenuation or amplification of the signal
Use the volts / div control to adjust the amplitude of the
signal before it is applied to the vertical deflection plates.
2.The time base
Use the sec/ div control to set the amount of time per division
represented horizontally across the screen.
3.The trigger level of the oscilloscope
Use the trigger level to stabilize a repeating signal, as well as triggering on a single event. .
总之，在使用一个模拟示波器时，需要根据输入信号，调节
以下3个基本的设置（钮）使示波器显示适当的信号图像。
1．信号的衰减或放大
用电压／单位格控制旋钮调整输入信号（到垂直偏离板之前
的）幅度。
2．时间基准
用秒／单位格设置旋钮设置屏幕上水平线每单位格所表示的
时间。
3．示波器触发控制旋钮
用触发器对准（钮）来稳定一个重复（周期）信号或触发一个单信号（无周期）。
自动化专业英语

## Slide 46
probe [prəub] n. 探针；调查 vi. 调查；探测 vt. 探查；用探针探测
attenuator [ə'tenjueitə] n. 衰减器；弱化子
deflection [di'flekʃən] n. 偏向；偏差；挠曲
dot [dɔt] n. 点，圆点；嫁妆 vi. 打上点 vt. 加小点于
glowing ['ɡləuiŋ] adj. 灼热的；鲜艳的；热情洋溢的 v. 发光；容光焕发phosphor ['fɔsfə] n. 磷光体，磷光剂
trigger ['triɡə] vt. 触发；引发，引起 vi. 松开扳柄 n. 触发器；扳机
stabilize ['steibilaiz] vt. 使稳固，使安定 vi. 稳定，安定
New words and phrases
自动化专业英语

## Slide 47
trace [treis] vi. 追溯；沿路走 vt. 追踪，查探；描绘n. 痕迹，踪迹
accommodate [ə'kɔmədeit] vt. 供应；使适应；容纳 vi. 适应；调解
attenuation [ə,tenju'eiʃən] n. 衰减；变薄；稀释
amplitude ['æmplitju:d] n. 振幅；广阔；丰富，充足
horizontal sweep 【电子学】水平扫描
自动化专业英语

## Slide 48
1. What do you need to know in order to better understand the oscilloscope controls? ?
2. Do you know what “horizontal sweep” is referring to?
3. In conclusion, when using an analog oscilloscope, what do you need to do?
Exercises
I．Answer the following questions according to the reading．
自动化专业英语
To better understand the oscilloscope controls, you need to know a little more about how oscilloscopes display a signal.
Horizontal sweep is a term referring to the action of the horizontal system causing the glowing dot to move across the screen.
In conclusion, to use an analog oscilloscope, you need to adjust three basic settings to accommodate an incoming signal.

## Slide 49
水平扫描放大器
2. 用信号衰减器或者用放大器
3. 模拟示波器是如何显示一个测量信号的？
4. 为了稳定一个重复（周期性）的信号，触发是必要的。
II．Translate the following into English．
horizontal sweep amplifier
use a signal attenuator or an amplifier
How does an analog oscilloscope display a measured signal?
The trigger is necessary to stabilize a repeating signal.
自动化专业英语

## Slide 50
示波器是如何工作的
为更好地掌握示波器的操作方法，你需要知道示波器是怎样显示信
号（图像）的。
当把示波器的探头与一个电路相连接时，电压信号通过探头送到示
波器的垂直系统，图5-4 是一个简单的线框图，说明一个模拟示波器是
怎样显示一个测量信号的。
当设定了垂直单位（电压／单位格）时，就确定了是用衰减器还是
用放大器（把输入信号转换成适当幅度的电压信号）。
接着，信号直接传到阴极射线管的垂直偏离板上，施加到这些偏离
板的电压大小导致发光点的移动（一个电子束撞击阴极射线管内部磷（
荧光物质）上产生光点），一个正电压使光点向上移动，而一个负电压
使光点向下移动。
译文：
自动化专业英语

## Slide 51
同时信号也输入到触发系统去启动或触发一个“水平扫描”，水平扫
描是一个专业术语，是指水平系统的作用导致光点沿着屏幕（水平）移
动，水平系统的触发导致水平扫描发生器驱动光点在一个指定的时间间
隔内从屏幕的左边移到右边。快速有序多次扫描导致这些光点的移动混
合成一条实线。以高速扫描的示波器，每秒中扫过屏幕的光点可能高达
50 万次。
水平扫描和垂直偏离的作用合在一起就在屏幕上形成了信号的图像轨
迹。为了稳定一个重复（周期性）的信号，触发器是必要的，它保证在
重复（周期性）信号的同（相位）点开始扫描，进而产生一个清晰的图
像，如图5-5 所示。
自动化专业英语

## Slide 52
总之，在使用一个模拟示波器时，需要根据输入信号，
调节以下3个基本的设置（钮）使示波器显示适当的信号图
像。
1．信号的衰减或放大
用电压／单位格控制旋钮调整输入信号（到垂直偏离板
之前的）幅度。
2．时间基准
用秒／单位格设置旋钮设置屏幕上水平线每单位格所表
示的时间。
3．示波器触发控制旋钮
用触发器对准（钮）来稳定一个重复（周期）信号或触
发一个单信号（无周期）。

## Slide 53
1.万用表
万用表是一种通用仪表，可用来测量直流和交流电压、
电流、电阻，有的还能测量分贝（放大倍数的情况）。有两
种万用表：一种是用指针在标准刻度上的移动来指示测量值
的模拟万用表（见图5-1 a），另一种是用电子数字显示器
显示测量值的数字万用表（见图5-2 b）。这两种万用表都
有一个正极（+）插孔和一个公共端（-）插孔用来插入测试
笔，一个功能选择开关用来选择（测量对象）：直流电压、
交流电压、直流电流、交流电流或电阻（欧姆值），一个范
围选择开关用来（选择范围）以测出精确读数。万用表还可
能有其它插孔用来测量高电压（1～5kV)和大电流（高达
10A），对一些特殊的万用表而言，还会有一些其它功能上
的变化。

## Slide 54
除了功能选择开关和范围选择开关（有时它们合成
一个开关），模拟万用表可能还有一个极性开关，可以很方
便地交换测试笔的极性。通常有一个螺丝可调节指针，（在
无电流时）使指针指在零处，另外当测量电阻时一个零点调
节控制（钮）用来对电池电压不足时做补偿调节（即保证电
阻为0时指针指向零值）。模拟万用表可以测量正电压和负
电压，只要简单地对调一下两个测试笔或拨一下极性开关，
数字万用表通常会自动在显示器上指示出极性。

## Slide 56
2. 示波器
示波器（图5-2）是一个图像显示设备，它显示一个电
子信号的图像。当信号输入到示波器中时，就产生一个电子
束，该电子束被聚焦、加速并适当偏离，在阴极射线管的显
示屏上显示电压的波形。

## Slide 57
示波器通常显示电压信号如何随时间变化的图像：其垂
直轴Y表示电压，水平轴X表示时间。在示波器屏幕上的电
压波形的幅度可以通过数出电压波峰与波谷之间纵向距离的
厘米值来确定（图5-3）。将这厘米值乘上V/cm控制钮的
设定值就得到电压的幅度值。比如说，假若电压的峰-峰间
幅度为5cm，控制钮设在1V/cm处，那么，峰-峰电压值
为5V。

## Slide 58
用示波器的水平标尺可以测量时间值，时间测量包括测量
信号的周期、脉冲宽度和频率。频率是周期的倒数，所以一
旦知道了周期，频率就是用1除以周期即可得到。
一个波形的频率可以通过在水平方向数出该波形一个周期的厘米值来确定，将这厘米值乘上时间/厘米控制钮的设定值就得到它的一个周期所需的时间。例如，假定一个波形长4cm，控制钮设在1ms/cm，那么，周期是4ms，则频率可以用下面的公式算出：

## Slide 59
f = = = 250Hz
假定控制钮设在lOO/cm，则周期是400，频率为2.5kHz。
双踪示波器具有同时显示输入信号和输出信号的优点，可以
显示输出信号是否有失真和表示输入/输出信号的相位关系
，即两路信号的波形重叠在一起可以较好地显示出输入与输
出信号相位的差别。

## Slide 60
Thank you!